## Slide 1: Correlating Parameters of Heat Exchange in Condensers
Introduction
Methods
Measured Variables: inlet/outlet temperatures, heat transfer area, flow rates
Figure 1: Condensers studied in experiment
Cold Stream Flow Rates (m3/s): 9.58∙10-6, 2.08 ∙10-5, 3.29 ∙10-5
  Flow rates were tested in triplicate
Results
The heat transfer coefficient increased with cold stream flow rate for all trials except parallel flow in the Allihn condenser
The Liebig condenser has a larger overall heat transfer coefficient then the Allihn condenser and is therefore more effective.
Design Problem
The effect of condenser type and flow pattern on the overall heat transfer coefficient (U) was analyzed using the following:
Reynold’s number (NRe) was used to correlate relevant parameters of our system to the overall heat transfer coefficient
Leif Burgess, Nick Schedeler, Ryan Lamers
References
Transport Processes and Separation Process Principles, 4th ed., Prentice-Hall, Inc. Upper Saddle River, NJ, 2003, pp. 291-300.
Allihn
Parallel Flow
Liebig
Counter Flow
Steam
h
Condensation point
Water out
Water in
Figure 2: Process Flow Diagram
Chart: Flow Rate (m3/s)
| 9.5840521372436259E-6 | 2.0798668885191348E-5 | 3.2851511169513796E-5
Parallel | 569.7259 | 553.9619 | 626.2495
Counter | 549.8795 | 696.6886 | 836.3629
Figure 3: For the Liebig condenser, as the flow rate of the cold stream increased the overall heat transfer coefficient increased as well. The magnitude of this correlation was greater for counter flow.
Chart: Flow Rate (m3/s)
| 9.5840521372436259E-6 | 2.0798668885191348E-5 | 3.2851511169513796E-5
Parallel | 257.2807 | 254.3909 | 236.9926
Counter | 270.9304 | 319.6074 | 372.5217
Chart: Reynold’s Number of Cold Stream
| 1069.5807224243847 | 2236.36990018898 | 3618.6898522311508
Parallel | 257.2807 | 254.3909 | 236.9926
Counter | 270.9304 | 319.6074 | 372.5217
Chart: Reynold’s Number of Hot Stream
| 7758.6428767257557 | 8313.7693673012491 | 8793.8787645557331
Parallel | 257.2807 | 254.3909 | 236.9926
Counter | 270.9304 | 319.6074 | 372.5217
Figure 5: Dimensionless comparison to the overall heat transfer coefficient for the hot flow stream
Figure 4: For the Allihn condenser, as the flow rate of the cold stream increased the overall heat transfer coefficient increased with counter flow and decreased with parallel flow.
Figure 6: Dimensionless comparison to the overall heat transfer coefficient for the hot flow stream
 | q | (1)
 |  | (1)
 |  | (2)
 |  | (2)
600 SCFM Steam
Water
Th,i = 100˚C
Th,o = 100˚C
Tc,o
Tc,i = 15˚C
Determine outlet temperature, and inner/outer diameter
Water in
Water out
Calculate Di
Compare cold stream flow rate to max U
Compare cold stream to max U
Calculate Do
Use Eq. 1 to calculate Tc,o
Final Answers:
Inner Diameter= 38.195 mm , Do= 38.199 mm, & Tc,o= 16.59˚C
Compare to max U