## Slide 1
UNH Baja SAE
Off-Road Racing Vehicle
The purpose of UNH Baja is to design, fabricate, and race a single seat, all-terrain, sporting vehicle within the regulations set by SAE.
During competition the vehicle is tested for endurance, acceleration, maneuverability, and hill-climb capabilities.
Personal Goals (Minimize Weight, Cost, etc.)
Background/Objectives
Drivetrain Design
Transmission
Gearbox is a Spicer H-12 FNR transaxle with a set 13.25:1 gear ratio
All components are internal (no external sprockets or chain drive) to reduce debris interference during competition
Custom axles fabricated from ATV and UTV axles
Includes: Forward, Neutral, and Reverse
Controls Design
Braking
Two hydraulic brake cylinders (front and rear) provide redundancy in case of failure
One pedal control to ease drivability
Bias bar for a front-rear braking ratio of 70:30
Pedals mounted from above to reduce interference on the floor
Polaris Outlaw 525 front calipers
Arctic Cat Mudpro 1000 Rear Calipers
  ¾” Bore Wildwood Cylinders
Steering
Rack & pinion steering
Turning radius of 12’
Detachable quick-release steering wheel
Thanks to Our Sponsors
Shea Family
Todd Gross
UNH Baja Group Members
Cole Gustafson
Jon Ulrich
Ted Withers
Suspension Design
Figure 3: Lotus Suspension Analysis view of complete suspension
Suspension Geometry Parameters | Front | Rear
Camber Toe Angle | 0° at Rebound -5° at Bump | 0° at Rebound -10° at Bump
Caster Angle | 3° at Static Ride Height | 0°
Toe Angle | -1° at Static Ride Height | 0°
Wheel Travel | 3” up 7” down | 3” up 8” down
Track Width | 52” | 50”
Static Ride Height | 11.5” | 11.5”
Front and rear double a-arm to allow a fully independent suspension
Fox Float Airshox chosen for vehicle shocks
Figures 4 and 5: SolidWorks finite element analysis load simulation given a 5ft drop
 | Static Rest | 5ft Drop
Maximum Stress | 14.6 MPa | 311 MPa
Maximum Displacement | .017 mm | .462 mm
Safety Factor (at max SCF) | 30.82 | 1.45
Shifting
Jetski Steering Cable to shift the transmission
Frame Design
Goals
Maintain driver safety
Minimize weight
Maximize structural integrity
Load-case | Max Deflection | Max Stress
Collision (30 mph) | 0.452 inches | 798 psi
Steel | Cost $/ft | Weight lb/ft | Outer Diameter (inches) | Thickness (inches) | Tensile Strength (psi) | Yield Strength (psi) | Weldability
A500 | 5.05 | 1.14 | 1.05 | 0.113 | 72,300 | 65,700 | Easy MIG/TIG
A513 | 8.80 | 0.50 | 1.00 | 0.049 | 98,740 | 86,530 | Easy MIG/TIG
Marc-Mentat FEA Results
Steel Selection: Our steel was chosen to meet competition requirements
while maintaining a high strength to weight ratio, low cost, and
to simplify welding requirements.
Alex Kachuck
Damon Tarry
Kevin Quinn
Tim O’Neil
Anthony Tonelli
Devan Shea
Engine
Engine: 10 Horsepower Briggs & Stratton
CVT driven, allowing engine to develop peak power at nearly all ground speeds
Figure 6: Plot of horsepower and torque vs. revolutions per minute. Max allowed RPM is 3800 producing 8HP and 11.8ft-lb of torque
Figure 1: Marc-Mentat Finite Element Analysis to test frame under torsion, loading, and impact
Figure 2: SolidWorks frame model showing A500 steel in blue and A513 steel in magenta