## Slide 1
Energy and Water Resource Efficient Production of Microalgae Lipids
Kelsey Price, Chemical Engineering Dept., University of New Hampshire, Durham, NH 03824
Background
Results
Conclusions
Future Investigations
Goal/Objectives
Methodology/Techniques
Algae require nutrients, light, CO2 & a water medium to grow in a photobioreactor (PBR) and produce lipids
Lipids are hexane solvent-extracted from algae
Lipids (algae oil) are feedstock to renewable biodiesel
Goal: Determine energy and fresh water efficient conditions to grow algae rich in lipids/oil
Objectives: To study:
Replacement of Fluorescent light with LEDs
Oil production in waste water vs. fresh water
Light intensity effect on lipid/oil production
Monitor algae growth with spectrophotometer turbidity readings and microscope cell counts
Effect of light and water source on lipid production
(Chlorella C2 Algae Lipid Production, mg lipids/L Solution-day)
LEDs influence the production of more lipids, and waste water lipid results are comparable if not better
Effect of light intensity on lipid production
(Chlorella C2 Algae Lipid Production, mg lipids/L Solution-day)
8000 LUX
2000 LUX
Fluorescent
Red LEDs
5500 LUX
2000 LUX
A higher light intensity influences a greater lipid production.
LEDs produce more lipids than fluorescent lighting, while saving energy
A greater light intensity increases lipid production
Waste water is a viable option for growing algae and conserving fresh water
In-situ production of Biodiesel (integrated lipid extraction and transesterification)
Reduced and effective nutrient solution specific to algae growth in waste water
Replace hazardous hexane lipid extraction solvent
  Less hazardous alternative
  Inexpensive alternative
Acknowledgments
Hamel Center for Undergraduate Research
Dr. Ihab Farag (Mentor)
Marian Elmoraghy
Dr. Nancy Whitehouse
Daniel Eltringham
Kristen Blackwell
John Newell
Dover Wastewater Treatment Facility
Process
Grow algae in PBR using Fluorescent light and Red and Red-Blue LEDs (48% less energy)
Measure light intensity in LUX
Monitor algae growth
Harvest/dry algae, get algae production rate
Extract oil and determine algae oil content
Algae Growth Stages:
Algae Pros & Cons
Advantages | Disadvantages
No food vs. fuel concerns Reduce land requirements Consume CO2 while growing | Fresh water consumption Energy Intensive Unfavorable economics
Scale Up: Effect of Water Source on Chlorella C2 Productivity and Lipid/oil Concentration in 80L PBR, 8000 LUX Fluorescent Light
Waste water produces more algae, and comparable lipids
Results
Measured Turbidity:
m
PBR
PBR