## Slide 1
L
Horizontal Cooling Towers: Thermal Regulation By Rivers
Support Electricity Generation in the Northeastern United States
Conclusions
University of
New Hampshire
Water Systems
Analysis Group
Introduction:
Questions:
What proportion of northeastern U.S. electricity production depends on engineered approaches vs. ecosystem services by rivers for cooling of waste heat?
What are the tradeoffs and unintended consequences of relying on ecosystem services in terms of altered temperature regime and fish habitat?
Rationale:
Thermoelectric power plants generate 90% of US electricity, and cooling them requires the single largest share of freshwater withdrawals.
Re-circulating approaches rely on engineered cooling and consumptive water use, while “once-through” depend one ecosystem services (cooling) in rivers, which comes at cost of elevated temperatures until re-equilibration is achieved.
We must understand river’s natural ability to mitigate heat loads in face of increased energy demands and changing climate. This ability is a function of various ecosystem properties, river flow, runoff, and atmospheric conditions.
The balance of energy use and cooling strategies will affect fish habitat, either through flow regime (consumptive use) or temperature regime (“once-through”)
Approach: Use a daily time-step, spatially-distributed, dynamic, river network hydrology and water temperature re-equilibration model linked to a thermoelectric energy model to quantify the relative importance of each type of cooling strategy, their impacts on rivers in the northeastern U.S., and ecosystem services provided by river systems to attenuate thermal pollution.
R.J. Stewart1 (rob.stewart@unh.edu), W.M. Wollheim1,2, A. Miara3, C.J. Vörösmarty3, B. Rosenzweig3, B. Fekete3
(1) Earth Systems Research Center, University of New Hampshire, Durham, NH, (2) Department of Natural Resources and Environment, UNH, (3) CUNY Environmental Crossroads, CCNY, NY
L
Model and Data:
Re-Equilibration of Water Temperatures during Routing*
Framework for Aquatic Modeling in the Earth System (FrAMES) for simulation of hydrology and runoff temperatures
Dingman (1972) for re-equilibration of water temperatures to atmospheric conditions during discharge routing
Thermoelectric Power Plant Model (TPPM, Miara 2012) for dynamic calculation of power generation, water use, and thermal pollution
Climate datasets acquired from MERRA (2000 through 2010)
Power Plant data assembled from UCS and EIA databases
Water
Temperature
Geometry
Cloud
Cover
Solar
Radiation
Wind
Speed
Initial
Water
Temp.
Air
Temp.
Energy Exchange
Function
Relative
Humidity
Flow Rate
Validation:
“Once-through”
“Re-circulating”
< 0.00
0.00 to 0.25
0.25 to 0.50
0.50 to 0.75
0.75 to 1.00
Nash-Sutcliffe
Coefficient
0
5
10
15
20
25
30
0
5
10
15
20
25
30
Mean Observed Water Temperature (oC)
Mean Modeled Water Temperature (oC)
Model output was compared with observed
temperatures at 242 USGS gauges (DA > 200 km2)
Mean annual water temperatures are most accurate in large rivers (DA > 2000 km2), but performance is good across entire spectrum
Modeled water temperatures accurately
represent daily water temperatures in region
MAE = 2.7
Heat Generated at Thermoelectric Plants
Impacts on Water Temperature
Basin | % Total Ann. Heat to Eng. | % Total Ann. Heat to Rivers | % Heat Atten. by Rivers | % Ann. Flow Withdrawn | % Ann. Flow Consumed
Conn. | 11.0 % | 47.9 % | 14.7 % | 19.5 % | 0.02 %
Merr. | 11.7 % | 38.9 % | 11.7 % | 6.40 % | 0.03 %
Susq. | 32.6 % | 28.5 % | 39.9 % | 15.5 % | 0.35 %
Region | 30.3 % | 22.5 % | 24.3 % | 5.51% | 0.14 %
Elec.
Eng.
Cooling
Other Heat Sinks
Total Heat
To Rivers
Elec.
Eng.
Cooling
Other
Excess Heat Leaked to Ocean
Heat Attenuated
By Rivers
Winter
Summer
Allocation of Total Heat Generated by Plants
(Northeast Region)
Power plants in the northeast rely as heavily on rivers as they do on cooling towers for heat dissipation during power generation
Re-equilibration of water temperatures to atmospheric conditions attenuates a significant proportion of total heat input to rivers during winter months
Consumption of water for evaporation in cooling towers is relatively minor
Model Domain and
Power Plant Locations
* Dingman, 1972
Comparison at
USGS Gauges
Percent of Total River Length Above Temp. Threshold
20o C
26o C
30o C
Dashed lines:
Scenario w/o
Power Plants
Unsuitable Habitats for Fish
(Cold = 20 oC, Cool = 26 oC, Warm = 30 oC)
Temp. Increase
Due to Plants (oC)
Thermal pollution from power plants leave a considerable footprint on avg. water temps
Avg. Summer
Nearly 1,700 km of river
length is increased at least
1 oC during the summer
Re-equilibration with atm.
conditions is more rapid
during the winter
Power plants slightly elevate water temperatures above critical thresholds for cold water fish.
Warm water fish are the most heavily impacted.
River networks (horizontal cooling towers) are 24.3% effective in dissipating heat and account for the cooling of 30.3% of the total heat generated for electricity production in the northeast US.
The cost of using this ecosystem service is an increase in the total unsuitable habitats habitats for cold, cool, and warm water fish by 0.2%, 5.6%, and 11.1%
Impacts in terms of river length are more widespread during the summer due to the reduced efficiency of re-equilibration associated with warm ambient atmospheric conditions
Engineered technologies such as re-circulating cooling towers have minor impacts on flow regime and often reduce river temperatures due to cold return flows
This highlights the buffering capacity of river networks to mitigate anthropogenic impacts to the system, and represents an important ecosystem performed by rivers in the northeast
National Science
Foundation