## Slide 1
Accelerated Bridge Construction
Bunker Creek Bridge, Durham NH
By: Elizabeth Kinney
Advisor: Dr. Charles Goodspeed
Background:
Originally built in the 1930’s
Various repairs through the year
Substructure mostly original
Considerations:
High Traffic Volume/Truck Route
Long Detour
Environmentally Sensitive Area
Oyster River
Bunker Creek
RT 4
Project Concepts
Use ABC methods to complete project as quickly and efficiently as possible using mostly precast/prestressed concrete members
Initial Site Work - minimal daily lane closures
Site Preparation
Column Installation
Bridge Replacement – Full Road Closure
5 to 14 days
Remove current bridge
Install new bridge
Post Site Work- minimal daily lane closures
Stone Wall Installation
Shoulder Widening on roadway
Columns
Pilecaps
NEXT D Beams
Roadway Widening
Drilled Shaft 1 ft outside of current roadway.
Cast in place with early high strength concrete.
Shaft will need to extend to +40’ in order to create a moment connection to bedrock. Surrounding soil is clay/silt mixture.
Precast offsite
Current NH truck limit for 8 or more axles is 150 kips without special permits.
Design without cutout was 176 kips, but with cutouts is 148 kips (using 7 ksi concrete)
SIDE VIEW
CROSS SECTION
Granite blocks stacked vertically and tied into bank in order to create a steeper slope that remains within current bank width.
Area will be filled in using geotextiles.
After compaction, a wider shoulder can be added and guard rails moved outwards.
4- 10’ wide NEXT 32 D beams will be used. Due to Flange width, no additional concrete is needed for deck.
Beams will be prestressed, precast off site.
Shear connections between the four NEXT 32 D beams will be accomplished with a Tongue and Groove Shear Key that is sealed with a polymer.
Post tensioning will be done using DYWDAG bars. Due to 2% hunch needed in roadway, a coupler will be cut/welded to match the slope. Computer modeling foresees negligible stresses across the center from the hunch, however laboratory tests still need to be accomplished.
NEXT 32D
Carbon Fiber-Reinforced Polymer (CFRP) grid will be used on top and bottom of flange in place of traditional Temperature and Shrinkage Steel.
Portsmouth
Durham