## Slide 1
A Distributed Sensor Network to Monitor Soil Responses to Climate Change
Brian T. Godbois1, Alexandra R. Contosta1, 2, Serita D. Frey1, Gopal K. Mulukutla2, Chris S. Cook1,2, Mary E. Martin2.
1 Department of Natural Resources and the Environment, University of New Hampshire
2 Earth Systems Research Center, Institute for the Study of Earth, Oceans, and Space, University of New Hampshire
Methods:
Properties—Continuous measurement of soil temperature, volumetric water content (VWC), electrical conductivity (EC), air temperature, barometric pressure, snow depth, wind speed and precipitation.
Pools—Assessed by analyzing soils for total C & N and bulk density.
Fluxes—Soil respiration is quantified continuously using automated chambers, soil profile sensors, and snow towers (for winter measurement through snow pack).
Sensor data collection strategy:
Soil sensors collect VWC, EC, temperature, and soil CO2 concentration data.
Weather sensors collect ambient outside air temperature, wind speed, snow depth, precipitation input, and chamber box temperature.
One autochamber is randomly selected and sampled for CO2 flux.
Loop repeats, data is sent via telemetry back to UNH for quality assurance and quality control analysis and then pushed to the web for visualization.
Remote sites are powered from solar and their sampling strategy is one acquisition loop per hour or can be less often as solar inputs change with the season.
Links to aquatic ecosystems:
Changing climate in terrestrial ecosystems can affect water balances and nutrient dynamics.
Water balances can be affected by precipitation and soil moisture content inputs which can impact stream discharge.
Nutrient dynamics from soil microbial activity in response to climate change can alter soil solution chemistry including DOM and inorganic N export into streams.
Contact info:
brian.godbois@unh.edu
Background:
Soil is vital for maintaining ecosystem quality and sustaining the function of ecosystem services. Soil organisms recycle organic matter into usable forms, driving nutrient cycling. Soil provides a building block for terrestrial ecosystems and a buffer for aquatic systems. Using in-situ sensors, we are quantifying the rate at which nutrients move through the environment with a changing climate.
Objectives:
1. Examine how soil properties and processes change spatially and temporally as climate in the region changes by monitoring soil carbon (C) pools and fluxes at multiple sites across the state of New Hampshire.
2. Link soil processes to water chemistry parameters by co-locating terrestrial and aquatic sensor sites.
3. Provide input to ecosystem models used to predict how ecosystems in the region will respond to climate and land-use change.
4. Stream live data to the web as an outreach and teaching resource.
Map By: Lucie Lepine