## Slide 1
Flow Separation Phenomena In Shear Wake/Cylinder Interaction
Team Members: Michael Auger, Douglas Carter, Amanda Makowiecki
Introduction
Findings
Discussion
Visualization Method
Future Study
Advisor: Dr. Joseph Klewicki
Hydrogen bubbles are an excellent way of tracking flow due to their nearly neutral buoyancy. They are created by running a current through a thin steel wire, causing hydrogen bubbles to be liberated from the water.
An argon ion LASER is passed through a cylindrical lens and creates a laser sheet that spreads along the axis of the cylinder. When the hydrogen bubbles pass through the laser sheet they brightly reflect the light.
A shear wake is special flow situation in which two boundary layer flows come together at the end of a splitter plate. The region in which the two flows meet is a region of reduced velocity.
When the shear wake encounters a uniform adverse pressure distribution (created in this project with a cylinder) an array of horseshoe vortices are produced. Investigating the characteristics of these vortices is the purpose of this study.
Increasing Reynolds Number (S.R.= 0.04)
The balance between shear ratio and Reynolds number has important consequences on the resulting vortex formation characteristics. An increase in Reynolds number encourages the development of vortices. At low Reynolds number, only partial vortex formation is observed, but as it increases the number of well developed vortices increases.
Large shear ratio shifts vortices away from the side with a dominant velocity and suppresses the formation of vortices. This is supported by data that indicates that only one partial vortex is observed at moderate Reynolds numbers for high shear ratios.
Although an increase in Reynolds number promotes the development of vortices, eventually too much inertial force destabilizes the vortex system and it becomes unsteady. For this study unsteadiness was observed at Reynolds numbers of approximately 750.
For a more comprehensive understanding of the vortex system, velocity measurements need to be taken in the region upstream the cylinder.
Use of laser Doppler velocimetry would allow for three dimensional velocity data to be obtained and assembled for a more complete description of the shear wake interaction.
Future study will hopefully yield a more quantitative understanding of the underlying mechanics behind the generation of the horseshoe vortex system.
Increasing Shear Ratio ( = 500)
Reynolds number based on cylinder diameter.
Shear Ratio, determined using the velocity on each side of the wake
Primary Variables
S.R. = 0.16
S.R. = 0.39
S.R. = 0.41
S.R. = 0.59
, S.R. = 0.12
Vortex System Characteristics as a function of Reynolds Number and Shear Ratio