## Slide 1
Introduction
Method
Future Work
This magnetometer is approximately 4 cubic centimeters. It was built and photographed by Chrystal Moser.
The magnetometer boom for CubeSat Sigma, a South Korean satellite that UNH is building a magnetometer for, has flaws that can be used to create a more effective boom to use on future satellites.
A magnetometer is a device that measures the intensity and direction of magnetic fields.
A magnetometer needs to be held away from the spacecraft or satellite so that magnetic fields generated by the magnetometer’s carrier do not influence or alter the data.
The magnetometer boom is what holds the device away from the satellite.
The motivation behind the project is that the boom set to go up on CubeSat Sigma could be improved and used on future satellites.
A CubeSat Sigma that will be sent up with a magnetometer from UNH. Picture courtesy of Dr. Marc Lessard.
Goals
Acknowledgements
Problems
Create a more compact design.
Make a sturdier boom that is stiffer and strong in multiple directions.
The current boom on CubeSat Sigma is too large.
The boom is strong in one direction but weak in another.
The design for the magnetometer boom relies on the pieces snapping together so that they are sturdy.
Build a mechanism for deploying the boom.
Continue to experiment with tab edges to find the best possible length and width.
A CubeSat is a satellite built of U’s. One U is a 10cm cube. These cubes are put together to house the instruments the satellite will carry.
CubeSat Sigma is 3U.
An example of a 3U CubeSat.
Krebs, Gunter D. "CubeSat." CubeSat. 1996. Web. 22 July 2014.
This design is a modification of Dr. Marc Lessard’s original concept.
Sarah Coffen (Winnacunnet High School)
Magnetometer Boom Prototype
Brass was used first as a test in principle.
The brass was not springy and did not hold the second part (SPbr) straight.
The Magnetosphere Ionosphere Research Lab, the University of New Hampshire, and Project SMART.
Advised and Aided by:
Dr. Marc Lessard
Chrystal Moser
Deployment Calculations
With the brass model of one of the hinges, a mechanism for extending the boom was fabricated.
Find a material that is more springy than carbon fiber that also is resistant to cracking and splitting.
A design for a boom deployment mechanism.
The next model of the joints for the boom was made of aluminium. The aluminium was not as springy or as strong as expected.
The third set of models was made of carbon fiber. It was a material chosen for its strength.
Three different models of the hinges were created.
Results
cf1
cf2
cf3
cf1
cf2
cf3
The support of the second part of the carbon fiber joints (SPcf) was best in the parts that had:
  Longer tabs
  A smaller opening
  Greater distance from the end of the tube to the pin hole.
The sturdiest joint was with the shape of cf2.
SPcf
SPbr
Advised and Aided by
Dr. Marc Lessard and Chrystal Moser
To deploy the boom, the main cable would have to be pulled approximately 1.4”.
Rpulley = 1/4”
Cpulley = π/4”
π/4” = π/8”
2
π/8” x 3.5 turns ≈ 1.4”
When the boom extends cable will shorten by half the circumference of the pulley at each joint.
There are three joints that open 180o and one that opens 90o, so that is 3.5 turns of the joints.
"Blue Planet Wallpaper." - Space Wallpapers. Web. 22 July 2014
Thanks to: Scott Goelzer (Coe-Brown Academy), and Louis Broad (Timberlane).