## Slide 1
Introduction
De-Spin Table
Acknowledgement: Research at the University of New Hampshire was supported by NASA and AFOSR grants.
De-Spun Rocket-Borne Imager for Auroral Observations
Marc Lessard1, Bruce Fritz1, Sarah Jones2, Allison Jaynes3, Paul Riley4
1. University of New Hampshire, Space Science Center, Durham, NH, USA; 2. NASA Goddard, Greenbelt, MD, USA; 3. University of Colorado-Boulder, Laboratory for Atmospheric and Space Physics, Boulder, CO, USA; Southwest Research Institute, Durham, NH, USA
Sponsored by NSF
TEC
Low Light Calibration
Rocket-based cameras provide a unique blend of spatial and temporal resolution that makes them a very attractive option for observing fine scale structure in the aurora. The flight characteristics of rockets makes the mechanical design of an imager challenging. The lateral motion of the rocket, the rotating motion of the payload, potential light pollution from the sun, and low light levels in the aurora all contribute to the design challenges. Several iterations of this imager design have flown on sub-orbital sounding rocket missions.
The imager is designed to observe aurora that is typically extremely faint and often sub-visual. The imager must be calibrated for low light levels. UNH has a class 10,000 clean room facility with a integrating sphere light source for calibrating a variety sensitive imaging equipment. The facility has been used to calibrate instruments for several rocket launches as well as satellite missions such as e-POP and MMS.
The rotating nature of many orbital and suborbital payloads requires a design that will counter-rotate at the same rate as the payload but in an opposite direction. The low-light level of the aurora we wish to image requires an integration time of 1 second and the counter-rotating allows us to avoid blurring the images as the light is accumulated.
This imager uses a 25 mm f/0.95 CCTV standard lens along with an e2v Back-Illuminated 2-Phas IMO Series Electron Multiplying CCD. The sensor has a 512 x 512 active pixel area that limits the field of view actually possible with the lens. Together the lens and CCD give the instrument has a 26° field of view.
In order to operate the EMCCD effectively it needs to be kept at a constant temperature near 0°C. This process generates a lot of excess heat inside of the imager assembly. The CCD electronics and power source are mounted on the rotating platform. As a result there is very little thermal contact between the power source and the rest of the imager housing, which means there is no efficient for heat to flow away. A heat sink is required to absorb as much of the excess heat as possible.
Optics
Baffle Assembly
A heat sink was designed to offer much volume as possible while staying within mass and volume constraints. The imager housing has a very limited volume with which to work.
In addition, extensive testing was done prior to the RENU flight to ensure that the CCD would maintain the proper temperature levels throughout the flight. More sophisticated methods would be required to transfer heat for a longer duration mission such as for a spin-stabilized spacecraft, but the TEC used here is sufficiently effective for the short duration rocket flight.
A model was developed using Solidworks to simulate the efficiency of heat transfer in the mechanical design. The simulations were used to help determine the amount of mass necessary for the heat sink to be effective
Heat Sink
CCD Contact Surface
TEC
Thermistor
The rocket missions the imagers in this heritage have flown on are typically on the nightside of the earth, but the northern latitude and high altitude apogee of the missions. This makes the imager optics susceptible to pollution from the sun and possible the moon from over the limb of the earth.
The baffle was designed mechanically as many separate pieces. This allows for easier machining of individual parts but also allows for a more modular design if any late changes were necessary. The aluminum surface is black anodized to reduce the reflectance of interior surfaces.
The cartoon shows the interior design to highlight the main components of the de-spin assembly. The DC motor drives a timing belt to turn the interior assembly. A photo-microsensor is used to monitor the true rotation rate of the assembly. The sensor output to the active feedback loop that controls the power of the motor. The rotating assembly.
The cartoon is from the ROPA rocket launch design. The upper stage and baffle have been modified for RENU 2 but the rotating assembly is essentially the same.
The integrating sphere is a SphereOptics LR-20 custom system designed for low light level calibration between 350 nm and 1000 nm
Despun rocket borne imager: Design aspects of a space based optical imaging instrument for auroral studiesEllis, Armin T. and Lessard, Marc R. and Bartel, Paul and Disbrow, Mike and Riley, Paul, Review of Scientific Instruments, 77, 045112 (2006), DOI:http://dx.doi.org/10.1063/1.2195102
Aurora Image credit: http://apod.nasa.gov/apod/image/0710/aurora_kuenzli_big.jpg
Image adapted from Ellis et al [2006]. Showing flight configuration and mounting of auroral imager as part of a suborbital payload. Diagram shows converging magnetic field (a), the spin axis of the payload and center of field of view (b), and footprint of the local magnetic field line within the imager’s field of view (c)
(c)
(b)
(a)
View of the imager with the lens exposed. 
 View of the imager in its ready to test configuration with the baffle installed.
View of the imager integrated into the aft-section of the RENU payload 
The rotating assembly is powered by a Maxon Motors 3.2 W DC motor assembly.
12 V nominal voltage
5030 rpm nominal motor speed
19:1, 2 stage gearbox
262 rpm nominal output speed
0.1 Nm output torque
The imager is spin calibrated in house to determine the power characteristics related to the de-spin mechanism. For the upcoming flight on RENU 2, the de-spin mechanism is coupled to a QRS-11 rate sensor in an active feedback loop to maintain a 1 Hz spin rate
Jones, S. L., M. Lessard, P. R. Riley and A. T. Ellis, Development of the DE-spun Rocket Borne Imager-2 in support of Rocket Observations of Pulsating Aurora, Proceedings of the 33rd Annual European Meeting on Atmospheric Studies by Optical Methods, Kiruna, Sweden, 28 August-1 September 2006, Ingrid Sandahl and Johan Arvelius (editors), IRF Scientific Report 292, 2008.
Lee, Y. S. (2000). A Baffle Design for an Airglow Photometer Onboard the Korean Sounding Rocket-III. Journal of the Korean Astronomical Society , 33, 65-72
Actual design dimensions of the imager baffle were calculated using a 26° field of view.
The baffle design process followed Lee [2000]. In principle the baffle is designed such that no optical components permitted to view an sunlit wall or vane edge directly. At least two reflections from darkened surfaces of the baffle tube or vanes are required between stray light sources and optical elements. Light from within the baffle is required to experience a maximum number of surface reflection from blackened surfaces before entering the objective lens. A minimum number of vane edges should be directly exposed to bright stray light.
Figures from Lee [2000]
The clean room is a custom designed and built facility capable of testing and calibrating space flight hardware.
Flight Heritage:
2004 – 35.035 – SERSIO
2005 – 40.017 – CASCADES
2007 – 40.020 – ROPA
2008 – 40.021 – SCIFER
2009 – 40.023 – CASCADES 2
2010 – 40.026 – RENU
(pictured)
CCD integrated in the circuit board in flight configuration. TEC is mounted directly below the board.
The flight lens for RENU 2 will be a UKA EL1025B, 25 mm F/0.95 CCTV lens
The figure above shows a simple equation for computing the angle (HEL) between a line-of-sight vector (or attitude vector) and Earth’s horizon (or limb). SEL is negative in the picture since SEL is defined positive when above the local horizon and HEL is defined positive when visible (i.e. above Earth horizon). Alpha is the difference (HEL – SEL).
SEL = solar elev. angle, rel. to local horizon
HEL = horizon elev. angle, rel. to Earth’s horizon
This angle allows us to compute the worst case scenario for line of sight from the payload to the sun or earth limb. This information is the starting point for computing the baffle blade dimensions.