## Slide 1: Heat Exchange in Condensing Systems Sofia Diaco, Zachary Lee, Samantha Nadeau Department of Chemical Engineering, University of New Hampshire
Results and Discussion
Methods
Introduction
References
.
Design Problem Solution
The purpose of this experiment was to determine the overall heat transfer coefficient for the different condensers in order to solve the design problem. The relationship is shown below, where T∞ is the condensation temperature.
Chose the straight condenser because it achieves higher heat transfer coefficients at higher flow rates
Chose counter current flow at heat setting 1 since this orientation led to the highest heat transfer coefficients
Assumed an outlet water temperature of 95 °C
Found diameter of condenser to be 15 cm
Found length of condenser to be 3.5 cm
Concluded that more testing would be needed
Tout-Tin decreased as cold stream flow rate increased
The overall heat transfer coefficient increases as the hot flow rate decreases
Counter-current flow results in higher overall heat transfer coefficients
Tin-Tout was similar with both counter current and co-current heat exchange
Water
15°C
Steam
100°C
600 SCFM
Steam
100°C
600 SCFM
Water
T=?
Chart: Cold Stream Flow Rate (m3/s)
| 7.31506666666666E-6 | 2.08285666666667E-5 | 3.43420666666667E-5
Power Setting 1 Counter-Current | 382.3151 | 708.2641 | 823.9452
Power Setting 5 Counter-Current | 367.5853 | 498.9695 | 575.7371
Power Setting 1 Co-Current | 304.4809 | 447.7482 | 320.8726
Power Setting 5 Co-Current | 373.6596 | 651.3437 | 726.6939
Found mass flow rate by counting the drops that condensed in a given time frame and then massing a certain number of drops
Kept Tc,in relatively constant
T. Bergman et al, “Heat Exchangers” in Introduction to Heat Transfer, 6th ed. New Jersey: Wiley, 2011. pp. 671-713.
C. Geankoplis, “Heat Exchangers” in Transport Processes and Separation Process Principles, 4th ed. New Jersey: Pearson Education, 2003. pp. 291-300.
Figure 1. Heat transfer coefficients increase as cold flow rate increases.
Chart: Cold Stream Flow Rate (m^3/s)
| 7.4819E-6 | 2.08285666666667E-5 | 3.45089E-5
Straight Condenser Co-current Flow | 373.6596 | 651.3437 | 726.6939
Straight Condenser Counter-current Flow | 367.5853 | 498.9695 | 575.7371
Curved Condenser Co-current Flow | 257.6957 | 409.8556 | 657.3232
Curved Condenser Counter-current Flow | 261.2293 | 436.9074 | 413.2866
Figure 2. The straight condenser was observed to achieve higher heat transfer coefficients.
Find: Type of Condenser, Orientation, Outlet Temperature, Area of Condensation
Water Flowmeter
Heating Mantle
Water inlet
Water outlet
Condenser
Water pump