## Slide 1: Heat Transfer Rates in a Condensing System Alexander Karam, Andrew Knight, Joseph Verro, and Joshua Beaudet, Department of Chemical Engineering, University of New Hampshire
Results
Methods
Introduction
References
Conclusions
[1] Geankoplis, C. J. (2014) Transport processes & separation process principles 4th ed. Pearson Education Limited Harlow
Overall Heat Transfer Coefficient (U) is dependent on flow rate and flow pattern.
Cocurrent flow resulted in greater heat transfer
As cold water flow rate increases the difference between flow types appears to increase dramatically
Acknowledgements
Department of Chemical Engineering, University of New Hampshire
Dr. Russell T. Carr
Figure 1. Allihn Condenser system fed with cold-water stream (20C) from feed pump and hot stream created with heating mantle.
Design Problem Solution
Using the temperature difference and mass flow rate, the heat transferred to the cold stream can be determined
Qwater = mCp ΔTwater
The heat of the water can then be used to calculate the overall heat transfer coefficient for the system
U = Qwater A ΔTlm
The Reynold number can then be related to the overall heat transfer coefficient and used for scale-up operations
Re = (DVρ)/μ
Figure 2: Relation between the overall heat transfer coefficient for counter current and co current flow types at a high and low volumetric flow rate.
 | Cocurrent |  | Countercurrent | 
 | 78 (mL/min) | 120 (mL/min) | 78 (mL/min) | 120 (mL/min)
ΔTSteam | 45 | 64 | 43 | 68
ΔTWater | 33.7 | 20 | 41.7 | 17.7
Table 1. The average difference in Temperature for each water stream over three measurements
68%
Discussion
The data collected was inconsistent due to the constraints imposed by the inaccurate and imperfect conditions of the condensing system
Other resources do not suggest a 68% difference between the overall heat transfer coefficient for cocurrent and countercurrent flows
What are the dimensions of the condenser, flow type, and exit temperature of the cold stream?
L=0.512 m
D=0.25 m
V=1.44 m/s
Temperature of Exiting Cold Stream: 53 Celsius
Flow Type: Cocurrent in a Allihn Condenser
Figure 3: The flow diagram for the scaled-up condensing system.
Flow Type | Flow Rate (mL/min) | U (W/m2K)
Cocurrent | 78 | 583
Countercurrent | 78 | 548
Cocurrent | 120 | 567
Countercurrent | 120 | 279