## Slide 1
Analysis and Comparison of Heat Exchangers
Double Pipe, Shell and Tube & Plate
Objectives
Introduction
Materials and Methods
Results and Discussion
Design Problem
Conclusion
Anthony Picone, Colin Graham & MaKenzie Marshall
University of New Hampshire Department of Chemical Engineering
Chemical Engineering Laboratory
Acknowledgements
References
Dr. Adam St. Jean and the Department
Of Chemical Engineering at UNH
Th,i, Th,o, Tc,i, and Tc,o recorded in triplicate for
counter and co current flow on each heat
exchanger type
Perform a Wilson Plot analysis to find the
average convection coefficients for each heat
exchanger.
Determine the effect of cooling water and
flow rate on the Overall Heat Transfer
Coefficient for each heat exchanger.
Use the data to find the most effective heat
exchanger and solve the design problem.
Double pipe [2]
Shell and Tube[2]
[2] Geankoplis, Christie J. Transport Processes And Separation Process Principles
(Includes Unit Operations). 4th ed. Prentice Hall, 2003. Print.
[3] Kushwaha, Ashish. “How Does A Plate Heat Exchanger Work?”. Quora. N.p., 2014.
Web. 30 Apr. 2017
[4] J. Fernandez-Seara, F. J Uhia, J. Sieres and A. Campco, “A general review of the
Wilson plot method,” ScienceDirect, 2007.
Key Equations
Rov = 1 = Ri + Rw + Ro (1)
U A
Q = m Cp ∆T (2)
Q= U A LMTD (3)
LMTD = ∆T2 - ∆T1 (4)
l n(∆T2∆T1)
Dh = 4 Ac [1] (5)
Pw
Plate Exchanger[3]
Determine heat rate
Determine temperature
difference
Determine hydraulic
diameter
Determine overall heat
transfer coefficient
[1] Kakaç, Sadık, Hongtan Liu, and Anchasa Pramuanjaroenkij. Heat Exchangers. 3rd ed.
Boca Raton: Taylor & Francis, 2012. Print.
Chart: Cold Water Flow Rate
| 3 L/min | 2 L/min | 1 L/min
Cocurrent | 1790.708 | 1363.4958 | 1171.5238
Countercurrent | 2116.7915 | 1783.4515 | 1539.352
Chart: Cold Water Flow Rate
| 3 L/min | 2 L/min | 1 L/min
Cocurrent | 1168.9591 | 1044.4179 | 858.3382
Countercurrent | 1205.3564 | 1118.2765 | 887.2405
Chart: Cold Water Flow Rate
| 3 L/min | 2 L/min | 1 L/min
Cocurrent | 2947.015 | 2535.1813 | 1827.5072
Countercurrent | 3088.2816 | 2641.3209 | 2142.1121
Chart: Cold Water Flow Rate
| 3 L/min | 2 L/min | 1 L/min
Plate | 5746.612 | 4154.6924 | 2386.2441
Shell and Tube | 5302.9 | 3984.1 | 2598.44
Double Pipe | 4878.9 | 3391.32 | 2282.23
Chart: 1/(Vn)
| 2.618185568446093 | 3.393898348209433 | 5.288810759786135
 | 0.0080953 | 0.0094689 | 0.011672
Figure 1. Overall Heat Transfer Coefficient for Double Pipe
Figure 2. Overall Heat Transfer Coefficient for Shell and Tube
Figure 3. Overall Heat Transfer Coefficient for Plate
 | Calculated Convection Heat Transfer Coefficient (ho) (W/m2K) | 
Heat Exchanger | Co-current | Countercurrent
Plate | 5941.46 | 5181.56
Shell | 1541.34 | 1643.31
Double Pipe | 2393.34 | 2346.47
Figure 4. Heat Transfer Coefficient for the cold stream in each heat exchanger with counter current flow
Figure 5. Wilson Plot Analysis for counter current flow in Double Pipe
Useful Data for Plate Heat Exchangers[1] | 
Unit | 
Largest Size | 1520 m2
Number of Plates | Up to 700
Plates | 
Thickness | 0.5 - 1.2 mm
Size | 0.03 - 2.2 m2
Spacing | 1.5 - 5.0 mm
Operation | 
Channel Flow Rate | 0.05 - 12.5 m3/hr
Performance | 
Heat Transfer Coefficients | 3000 - 7000 W/m2K
Design Solution
Heat Exchanger Type - Plate
Objective: Specify the type and dimensions of a
heat exchanger
Given Values for Design Heat Exchanger
Overall Heat Transfer coefficient higher
for counter current flow
Overall Heat Transfer coefficient
decreases with cold flow rate
Plate Heat Exchanger has highest Overall
Heat Transfer Coefficient
Shell and Tube has lowest Overall Heat
Transfer Coefficient due to lowest Q (eqn 2).
Heat Transfer coefficient decreases with
flow rate
Calculated Heat Transfer coefficient for
Plate is highest, Shell and Tube is lowest
Calculated and experimental values for
counter current are most accurate for
Plate
m ̇c | 3.0 kg/s
Tc,i | 20 ℃
Tc,o | 50 ℃
Th,i | 80 ℃
Original Wilson method used
Best fit was found when n = 0.85 (original study n = 0.80)
h calculated using slope and intercept
?
hi = C2 vrn
ho = 1 .
(C1- Rw) Ao
C2 = 1 .
A * slope
Intercept = C1
# of Plates | 15
Length | 0.20 m
Width | 0.1 m
Thickness | 1.2 mm
Effective Diameter | 3.4 mm
Tho | 70.0 ℃
LMTD | 39.15
mh | 3.11 kg/s
Flow Type | Counter Current
See Reference [4] for equations
Plate heat exchanger most efficient at exchanging energy
Larger volume flow rate of cold stream, greater overall heat transfer
coefficient
Counter current flow had higher heat exchanged
Using the Wilson Plot, the average convection coefficients for the hot and
cold water side were calculated in both flow patterns