## Slide 1
Production of Nylon 66 Using Bio-Based Feedstock
Sofia Diaco, Ami Humphrey, Jeffrey King, Marjorie Steiner
Objectives
Continuously and sustainably produce 85,000,000 pounds of nylon 66 per year
Design to run at 100% and 67% capacity
C2Q Variables
High molecular weight
Low moisture content
5 mm granulated pellets
Inherent Safe Design
Control Loops
Conclusions
Selling price of $3.24/kg yields DCFRR of 26.9%
Significant market potential (automotive)
Bio-based feedstock and ORC increase sustainability
Recommendations
Lady Power recommends a “GO”
Acknowledgments
Dr. Halpern, Dr. Vasudevan, Chemical Engineering Department, Kingsbury Library
Stream | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37
0 | Water | Water | Water | Adipic Acid | HMDA | HMDA | Salt | Salt | Steam | Salt | Salt | HMDA | Water | HMDA Solution | HMDA Solution | HMDA Solution | Nitrogen | Nitrogen | Nitrogen | Nitrogen | Vapor | Steam | HMDA | HMDA | Molten Nylon 66 | Steam | Molten Nylon 66 | Steam | Molten Nylon 66 | Molten Nylon 66 | Nylon 66 pellets | Nylon 66 pellets | Vent gases | Vent gases | Vent gases | Steam | Vent gases
Temperature (C) | 25 | 25 | 55 | 25 | 25 | 25 | 55 | 55 | 155 | 155 | 155 | 25 | 25 | 25 | 25 | 68 | 25 | 75 | 125 | 143 | 190 | 188 | 321 | 321 | 260 | 275 | 275 | 200 | 200 | 200 | 250 | 25 | 222 | 222 | 155 | 155 | 200
Pressure (barg) | 0 | 1 | 0.5 | 0 | 0 | 0 | 0 | 0.5 | -0.2 | -0.2 | 11.5 | 0 | 1 | 0 | 12 | 11.5 | 13 | 12.5 | 12 | 11.5 | 11 | 10 | 10 | 11.5 | 11 | 0 | 0 | 0 | -0.95 | 0 | 0 | 0 | 0 | 0 | -0.20 | -0.20 | 0.00
Vapor fraction | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1
Molar flow rate (mol/hr) | 164,060.5 | 155,104.5 | 155,104.5 | 27,050.5 | 21,512.4 | 9,016.8 | 173,623.9 | 173,623.9 | 140,254.1 | 33,369.8 | 33,369.8 | 12,495.5 | 8,956.0 | 21,451.5 | 21,451.5 | 21,451.5 | 5,000.0 | 5,000.0 | 5,000.0 | 5,000.0 | 44,739.4 | 43,492.4 | 1,247.0 | 1,247.0 | 49,846.0 | 28,175.5 | 21,670.5 | 117.8 | 21,552.7 | 21,552.7 | 21,552.7 | 21,552.7 | 71,667.9 | 71,785.7 |  |  | 
Mass flow rate (kg/hr) | 2,955.6 | 2,794.2 | 2,794.2 | 3,143.5 | 2,499.9 | 1,047.8 | 6,985.5 | 6,985.5 | 2,526.7 | 4,458.8 | 4,458.8 | 1,452.1 | 161.3 | 1,613.4 | 1,613.4 | 1,613.4 | 140.1 | 140.1 | 140.1 | 140.1 | 978.7 | 833.8 | 144.9 | 144.9 | 5,378.6 | 507.6 | 4,871.0 | 2.1 | 4,868.9 | 4,868.9 | 4,868.9 | 4,868.9 | 1,341.3 | 1,343.5 | 658.6 | 1,868.1 | 2,002.1
Components (kg/hr) | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 0.0
Adipic Acid | 0.0 | 0.0 | 0.0 | 3,143.5 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 0.0
HMDA | 0.0 | 0.0 | 0.0 | 0.0 | 2,499.9 | 1,047.8 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 1,452.1 | 0.0 | 1,452.1 | 1,452.1 | 1,452.1 | 0.0 | 0.0 | 0.0 | 0.0 | 145.2 | 0.3 | 144.9 | 144.9 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.3 | 0.3 |  |  | 0.3
Water | 2,955.6 | 2,794.2 | 2,794.2 | 0.0 | 0.0 | 0.0 | 2,794.2 | 2,794.2 | 0.0 | 267.5 | 267.5 | 0.0 | 161.3 | 161.3 | 161.3 | 161.3 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 510.5 | 0.0 | 2.9 | 0.0 | 0.8 | 0.8 | 0.8 | 0.8 | 0.0 | 0.0 |  |  | 0.0
Steam | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 2,526.7 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 693.4 | 693.4 | 0.0 | 0.0 | 0.0 | 507.6 | 0.0 | 2.1 | 0.0 | 0.0 | 0.0 | 0.0 | 1,201.0 | 1,203.1 | 658.6 | 1,868.1 | 1,861.7
Nylon salt | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 4,191.3 | 4,191.3 | 0.0 | 4,191.3 | 4,191.3 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 
Molten nylon | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 4,868.1 | 0.0 | 4,868.1 | 0.0 | 4,868.1 | 4,868.1 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 
Nylon 66 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 4,868.1 | 4,868.1 | 0.0 | 0.0 |  |  | 
Nitrogen | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 140.1 | 140.1 | 140.1 | 140.1 | 140.1 | 140.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 140.1 | 140.1 |  |  | 140.1
Objectives and C2Q Variables
Safety Considerations
Economic Analysis
Conclusions and Recommendations
NPT= 4 years
PBP=2.6 years
DBEP= 6 years
DCFRR=26.9%
Equipment Cost
Summary
Minimize
Substitute
Moderate
Simplify
Process Flow Diagram and Material Balance
Notes: This is only a template. You may chose to use or not use this format. I highly recommend you use a format that works for your group.