## Slide 1
An Examination of Heat Exchange in
Condensing Systems Jackson Kaspari, Sarah Lambert and Minghao Wei
University of New Hampshire, Chemical Engineering Department, Durham, NH 03824
Apparatus: Water Cooled Allihn Condenser
Methods
Results
Discussion
Introduction
Design Solution
References
Goal: Determine the effect of flow pattern and rate on resulting overall heat transfer coefficient. This will result in the development of parameter correlations essential to solving the design problem.
Acknowledgement: Dr. St. Jean and the University of New Hampshire Chemical Engineering department
When vapor condenses on a vertical plane or tube and flows due gravitational forces this is known as film-type condensation.1
Water based condensing systems are utilized for refrigeration, heat exchangers, chemical industries, and desalination units.2
Two types of flow in a condensing system
  Cocurrent
  Countercurrent: Known to be a more effective flow pattern
Cold water is circulated and flow rate is controlled using Isotemp Refrigerated Circulator Model 9100.
Boiling chips added to prevent bumping and ensure consistent boiling.
Flow pattern changed by swapping the line input positions.
↑ Flowrate causes ↓ residence time = ↑ U
T-test  all comparisons significant
Inconsistent pump  inconsistent flowrate  U error
Inability to dry condenser  heat transfer area uncertainty
Geankoplis,J C. Transport Processes and Separation Process Principles, 4th ed,; Prentice Hall: New Jersey,2011.
Charef, A.; Feddaoui, M. B.; Najim, M.; Meftah, H. Desalination2017, 409, 21–31.
Figure 1. Average experimental and theoretical overall heat transfer coefficient values for cocurrent and countercurrent flow patterns studied at 60(mL/min). Stars indicate statistical significance.
Figure 3. Range of mass flow rates (water) dependent on the outlet water temperature range. Values limited to those that satisfy the design problem.
Figure 2. Average experimental and theoretical overall heat transfer coefficient values for cocurrent and countercurrent flow patterns studied at 100(mL/min). Stars indicate statistical significance.
Conclusion
Error associated with pump flowrates led to unreasonable design U values. The best solution utilized countercurrent flow, has Twater,o=40°C at a flowrate of 36.5 kg/s and an area of 2.3x10-5 m2 and a height of 1.5x10-4
Using theoretical values for the design problem, at the same Twater,o and flowrate and a diameter of 0.05m the contact area of the condenser was 0.09m2 and the height was 0.6m
86000% Error
85000%
Error
*
30000% Error
34500% Error
*
*
*
*
*
*
*
Figure 4. Correlation plot used to predict a design U value based upon corresponding Reynolds numbers.
Figure 5. Contact area values of design condenser based upon a range of Reynolds numbers using 0.05m as the condenser diameter.
Notes: Cocurrent/countercurrent diagram