## Slide 1: Comparison of Heat Exchangers Double-Plate, Shell-and-Tube, & Plate Trevor Campbell, Thomas Higgins, Jaclyn Kinson Department of Chemical Engineering, University of New Hampshire
Results
Methods
Introduction
References
Discussion
Transfer of heat between two fluids in industrial processes are carried out by heat exchangers (e.g. oil and gas, energy production, chemical processes)
Heat exchangers can operate at both co-current and counter-current flow patterns
Co-current flow Counter-current flow
Hot Hot
Cold Cold
The log mean temperature difference method (LMTD) is used when hot and cold fluids are in true co-current or counter-current flow[1]
Without directly measuring surface temperature, Wilson Plots estimate the convection coefficients in heat exchangers[2]
[1] C. Geankoplis, Transport Processes and Separation Process Principles (Includes Unit Operations), 4th ed. New Delhi: Pearson India Education Services, 2016, pp 293.
[2] J. Fernandez-Seara, F. Uhia, J. Sieres and A. Campo, "A general review of the Wilson plot method and its modifications to determine convection coefficients in heat exchangers devices", Science Direct, pp. 1-13, 2007.
[3] “HT32/HT37: Plate Heat Exchangers”, Discoverarmfield.com, 2017. [Online]. Available: http://discoverarmfield.com/en/products/view/ht32-ht37/plate-heat-exchangers. [Accessed: 26-Apr-2017].
Counter-current flow patterns produce a greater overall heat transfer coefficient than
co-current flow patterns
Cold water flow rate increases, the overall heat transfer coefficient increases
Interestingly, U of shell-and-tube was the lowest value
    Likely because the cold water velocity was so small
Convection coefficient hot water > convection coefficient cold water
The convection coefficients of the Shell-and-Tube vary significantly
    Also, due to the small cold water velocity
Co-current convective heat transfer coefficients (h) seemed to be higher than
counter-current heat transfer coefficients for all three heat exchangers
Experimental Apparatus
Design Problem
GOALS:
Compare the overall heat coefficients for each heat exchangers at
co-current and counter-current flow rates, using the LMTD method
Perform a Wilson Plot Analysis to find the average convection coefficients of the cold and hot water
Solve the design problem
Double-Pipe: hot fluid flows through the inner pipe while the cold fluid flows through the outer pipe
1-1 Shell-and-Tube: hot fluid flows Plate: pack of plates in which hot and
through the 7 inner pipes while the cold fluid flow on opposite sides[3]
cold fluid flows through the shell with
cross baffles to induce cross-flow
Plate Heat Exchanger with Counter-Current Flow:
Assuming qhot = qcold, the mass flow rate of the hot stream and Tho was calculated using Excel Solver
m = 3.75 kg/s Tho = 329 K = 56 ºC
Assuming the spacing in between plates was 0.02 m and Rehot was constant in both the lab and scale-up schematics:
W = 1.039 m D = 0.221 m ʎ = 0.02 m
Experimental correlation of U vs. Recold and was used to find length
Ltotal = 3.609 m N = 5 Lplate = 0.723 m
Acknowledgments
Dr. Adam St. Jean
Funding provided by the Department of Chemical Engineering
Experimentation:
For each heat exchanger:
  Operated at co-current and counter-current flow patterns
  Measured the inlet and outlet temperatures of the hot stream (2 L/min, inlet set at 40 ºC) and the cold stream (3 L/min, 2 L/min, 1 L/min) in triplicate
Calculation Methods:
LMTD Method
co-current counter-current
Error and Statistical Analysis:
  Standard Error and T-Test (95% CI) within Excel
[1]
Conclusion
The overall heat transfer coefficients of a double-pipe, shell-and-tube, and plate heat exchanger were compared using the LMTD method
    The plate heat exchanger had the highest overall heat transfer coefficient
The average heat transfer convection coefficients were compared using the Wilson Plot method
    The Plate Exchanger had higher values than the Double-Pipe
A plate heat exchanger would be the best option to heat the fluid, as described in the design problem
    Dimensions: W = 1.039 m D = 0.221 m ʎ = 0.02 m Lplate = 0.723 m N = 5
    Hot Stream: Thot = 56 ºC mhot = 3.75 kg/s
Figure 1. The comparison of the overall heat coefficient of each heat exchanger A) Double-Pipe
B) Shell-and-Tube and C) Plate. The Plate Heat Exchanger has the highest overall heat transfer coefficient (U). For co-current patterns, the percent difference is 54.9% for Double-Pipe and 86.6% for Shell-and-Tube. For counter-current patterns, the percent difference is 44.7% for Double-Pipe and
89.4% for Shell-and-Tube. The stars represent statistically significant data.
Chart: Cold Water Flow Rate [L/min]
Con-Current | 904.7338 | 1091.9905 | 1181.0928
Co-Current | 868.2301 | 1049.0503 | 1189.3129
A)
B)
Chart: Cold Water Flow Rate [L/min]
Con-Current | 2340.2505 | 2777.9374 | 3137.9578
Co-Current | 2245.5636 | 2669.5748 | 2959.1738
C)
20 ºC
3 kg/s
50 ºC
80 ºC
m=? kg/s
Tho =?
Chart: 1/Vc0.82
| 0.20127445137068334 | 0.28066191487624509 | 0.49548222641186845 | 0.20127445137068334 | 0.28066191487624509 | 0.49548222641186845 | 0.20127445137068334 | 0.28066191487624509 | 0.49548222641186845
Counter-Current | 0.0098854 | 0.010623 | 0.013641 | 0.010207 | 0.010586 | 0.013842 | 0.010012 | 0.010794 | 0.012275
Co-Current | 0.0085465 | 0.009138 | 0.011333 | 0.0087658 | 0.0092356 | 0.011253 | 0.0086096 | 0.0093236 | 0.012056
Figure 3. The Wilson Plot of the Plate Heat Exchanger for both co-current and counter-current flow patterns. Using the slope and intercept of each trendline, the values of “h” were extracted for the hot and cold streams.
Chart: Cold Water Flow Rate [L/min]
Counter-Current | 1533.8941 | 1728.6004 | 1936.4295
Co-Current | 1286.4984 | 1456.2547 | 1705.4722
Dimensions of the Heat Exchanger:
ʎ=? W=? L=? D =?
Chart: Convection Coefficient [W/m2]
Counter-Current | 9469.3936 | 3109.2823
Co-Current | 10416.3329 | 3543.0584
Chart: Convection Coefficient [W/m2]
Counter-Current | 79466.5846 | 1994.6999
Co-Current | 113525.447 | 2052.3242
Chart: Convection Coefficient [W/m2]
Counter-Current | 10511.6032 | 3605.8756
Co-Current | 11656.4312 | 4360.6206
Figure 2. The comparison of the convective heat transfer coefficients of the hot and cold water for A) Double-Pipe B) Shell-and-Tube and C) Plate. The Shell-and-Tube Exchanger had both the highest value of hhot and the lowest value of hcold. The Plate Exchanger has higher coefficient values than the Double-Pipe Exchanger.
B)
A)
C)