## Slide 1
7
EVPFFT domain decomposition
A Domain Decomposition Parallel Implementation of an Elasto-viscoplasticCoupled elasto-plastic Fast Fourier Transform Micromechanical Solver with Spectral Database Constitutive Representation
Adnan Eghtesad, Timothy Barret, Kai Germaschewski, Ricardo A. Lebensohn, Rodney J. Mcabe, and Marko Knezevic
Department of Mechanical Engineering, University of New Hampshire, Durham, NH 03824, USA
Department of Physics, University of New Hampshire, Durham, NH 03824, USA
Materials Science and Technology Division, Los Alamos National Laboratory, Los Alamos, NM 87544, USA
MPI (Message Passing Interface)
* Facilitates communication among nodes of a cluster connected through high speed network *
* MPI uses domain decomposition for parallelization *
A multiscale plasticity approach which explicitly models discrete grains and slip systems to capture the microstructure anisotropy of material
What is crystal plasticity?
Slip systems
Macroscale homogenized model
Grain
Microstructure RVE
(Polycrystalline)
Crystal plasticity constitutive framework
1
Computational crystal plasticity
Crystal plasticity simulations are more accurate, predictive and robust comparing to macroscale plasticity but slow! One needs to accelerate them to facilitate further efficient research into this field
Fast CP simulations
Parallel run on cluster of CPUs (Domain decomposition)
Texture compaction
Parallel run on multiple GPUs
Non-iterative spectral solvers (Pre-computed databases)
2
https://www.hec.nasa.gov/news/features/2011/sbus_042111.html
Nasa advanced super computing (NAS) cluster with 29,368 computing cores
High Performance Computing (HPC)
Tools for Parallel computing on CPUs
OpenMP
MPI
Hybrid OpenMP-MPI
3
OpenMP (Shared memory parallel programming)
* Supports multi-threaded parallel programming on shared memory *
* Uses directives around loops to parallelize them *
4
5
EVPFFT (Elasto-viscoplasticCoupled elasto-plastic Fast Fourier Transform)
6
8
Profile the code (Performance Profiler)
9
Up to 95x Speedup on only 64 CPUs!