## Slide 1: Heat Exchange in Condensing Systems Caroline Houston, Brandon Blaesing, Thomas Lalouche, Tirthadeep Das Chemical Engineering, University of New Hampshire, Durham, NH 03824
Overall Heat Transfer Coefficient (U)
Conclusions
Background
Heat Exchange is important in many industrial processes
Overall heat transfer coefficient indicates effectiveness of heat transfer
Types of Condensation:
Film-type Condensation Drop-wise Condensation
Purpose
Study overall heat transfer coefficients in condensing systems
Effects of cold and hot stream flow rates and flow pattern
Determine correlations
Solve design problem
Introduction
Dr. Adam St. Jean, Department of Chemical Engineering, for advising
Department of Chemical Engineering, for funding
Acknowledgments
Assumptions:
Cylindrical shape
Counter Current
Same materials as laboratory scale
No fouling
Resistance from conduction is negligible compared to convection resistance
Scaling:
Type and Dimensions:
Counter current, Cylinder
Exit temperature: 45℃
Diameter:
Inner: 0.08m
Outer: 0.09m
Length: 75.2m
Effect of Heat Source:
Higher source temperature, decrease in overall heat transfer coefficient
Flow pattern constant
Effect of Flow Rate:
Inlet water flow rate increase, overall heat transfer coefficient increase
Flow pattern, heat source constant
0.0038kg/s – different trend
Effect of Flow pattern:
Higher overall heat transfer coefficient for counter current compared to co-current
Heat source constant
Design Problem
References
[1] S. Subramanian, http://ljournal.ru/wp-content/uploads/2017/03/a-2017-023.pdf, Thermal Analysis of a Steady Heat Exchanger, 2017
[2] P. Sabharwall, V. Utgikar, and F. Gunnerson, “Effect of Mass Flow Rate on the Convective Heat Transfer Coefficient: Analysis for Constant Velocity and Constant Area Case,” Nuclear Technology, vol. 166, no. 2, pp. 197–200, 2009
[3] C. J. Geankoplis, Transport Processes and Separation Process Principles, 4th ed. Pearson.
[4] “Engineering ToolBox,” Engineering ToolBox. [Online]. Available: https://www.engineeringtoolbox.com/. [Accessed: 30-Apr-2018].
Discussion:
Film of condensation – effect overall heat transfer coefficient
Increase steam flow rate, increase condensed water amount – effect overall heat transfer coefficient
Sources of Error:
Inaccurate measurements
Heat source fluctuated
Fouling
Film condensation
Future Work:
Higher steam flow rates
Observe overall heat transfer coefficient
Effects of fouling
Horizontal cylinder
Vapor
Cooled Wall
Vapor
Cooled Wall
Liquid Film
Liquid Droplets
Methods & Analysis
Chart: Flow Rate (kg/s)
CoCurrent LowHeat | 237.5497 | 348.2823 | 351.1677
CounterCurrent LowHeat | 390.0641 | 508.3539 | 441.2343
CoCurrent HighHeat | 257.3295 | 341.8902 | 334.8238
CounterCurrent HighHeat | 366.6338 | 452.9981 | 617.247
Dimensionless Numbers
Nusselt Number (Nu)
Prandtl Number (Pr)
Reynolds Number (Re)
Heat Transfer (U)
Log Mean Temperature ()
Chart: High Heat
| 0.0680013828624575 | 0.0680013828624575 | 0.0680013828624575 | 0.0566164201306501 | 0.0566164201306501 | 0.0566164201306501 | 0.0504844773283362 | 0.0504844773283362 | 0.0504844773283362
HighHeat CoCurrent | 0.5435 | 0.54918 | 0.53356 | 0.45909 | 0.51364 | 0.51214 | 0.50057 | 0.58257 | 0.46075
HighHeat CounterCurrent | 0.80399 | 0.61519 | 0.54899 | 0.65523 | 0.46205 | 0.58765 | 0.60317 | 0.56663 | 0.27967
Condensation
Apparatus
Flow: Co-current, Counter current
Inner Diameter: 0.014mm
Outer Diameter: 0.018mm
Ri
Ro
Steam
1 atm
Water
45 ℃
Steam
1 atm
Water
600SFCM, 15℃
Chart: Low Heat
| 0.0294513182961421 | 0.027756007277936 | 0.027756007277936 | 0.0217398498622203 | 0.0217398498622203 | 0.0217398498622203 | 0.0186585182827535 | 0.0186585182827535 | 0.0186585182827535
LowHeat CoCurrent | 0.61727 | 0.6924 | 0.58492 | 0.48883 | 0.53137 | 0.51122 | 0.53078 | 0.56231 | 0.52996
LowHeat CounterCurrent | 0.57661 | 0.51391 | 0.48875 | 0.47843 | 0.45872 | 0.37868 | 0.58419 | 0.52555 | 0.57959
Vertical Heat Exchangers
Assumptions
Film-type condensation
No sub-cooling of water after condensation
Constant heat source
Overall Resistance
Reynolds number constant during scaling
Re laboratory = Re scaling 
Nusselt number remain constant during scaling
Nu laboratory = Nu scaling 
(Heat transfer coefficient for water)
Nu laboratory = Nu scaling 
(Reynolds Number for steam)
Heat Transfer Coefficient
Overall Heat Transfer Coefficient