## Slide 1: Production of Dimethyl Ether from Methanol ROLO Engineers Serge Boucher, MaKenzie Marshall, Jia Mo, Joseph Verro Chemical Engineering, University of New Hampshire, Durham, NH 03824
Process Flow Diagram
Introduction
References
Acknowledgements
Market:
Transportation Fuel [1]
The global demand for dimethyl ether (DME) is continuously increasing and will grow to USD 11.72 billion by 2023 [2]
Product:
ISO DME Fuel Plant gate Standard (ASTM D7901.144734) [1]
Critical to quality variables:
Composition of 98.5 wt% minimum
Reaction:
Gas phase
Gamma Alumina Catalyst
35 barg and 325 ℃
Single pass conversion: 85%
Overall conversion: 99.99%
Capacity:
250,000 gallons per day at 100% [1]
125,000 gallons per day at 50%
Location:
Lake Charles, LA [1]
Conclusions
Safety Evaluation
Economic Analysis
Grass Roots Costs: $7.67 million
Total Capital Investment: $9.06 million
Plant is under construction for 2 years and operates for 20 years [1]
Chart: Manufacturing Cost
| Raw materials | Mathanol Transportation | Catalyst | Labor | Steam | Electricity | CTW and Demin Water | Waste Water | Operating Supplies and Maintenance | Laboratary Charges | Patents and Royalties | Overhead, Packaging, Storage | Local Taxes and Insurance
 | 0.90333 | 0.012179 | 0.001666 | 0.0029973 | 0.060522 | 0.00044368 | 0.0063607 | 4.5005e-05 | 0.0020279 | 0.00039095 | 0.0049747 | 0.0028564 | 0.0022043
Market price: $2.28/gal
Net annual profit: $1.97 Million
After tax rate of return: 33%
DBEP: 6 Years
PBP: 3.2 Years
Inherent Safe Design
A continuous process was used
Pipes are insulated to reduce the risk of burns
Pipes and equipment are labeled
Relief valves are designed
Initial HAZOP Report completed
Relief Valves
DME market is growing due to demand for more environmentally friendly fuels.
Proposed process: Pressurized, high temperature, gas-phase reaction over Gamma Alumina catalyst.
Net annual profit: $1.97 Million
After tax annual rate of return: 33%
Proper safety considerations were made to ensure smooth operation
This plant is a GO!
Thank you to the chemical engineering staff, our families and friends for their help and support through the four years at UNH
 | MW | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Stream 5 | Stream 6 | Stream 7 | Stream 8 | Stream 9 | Stream 10 | Stream 11 | Stream 12 | Stream 13 | Stream 14 | Stream 15 | Stream 16 | Stream 17 | Stream 18 | Stream 19 | Stream 20 | Stream 21 | Stream 22 | Stream 23 | Stream 24
Component | (kg/kmol) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CH3OH | 32.04 | 36018.8 | 36018.8 | 42395.6 | 42395.6 | 42395.6 | 42395.6 | 6383.8 | 6383.8 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 6383.2 | 6376.8 | 6376.8 | 6.4 | 6.4 |  |  |  |  | 
H2O | 18.02 |  |  | 10.1 | 10.1 | 10.1 | 10.1 | 10133.6 | 10133.6 |  |  |  |  |  |  | 10133.6 | 10.1 | 10.1 | 10123.5 | 10123.5 | 2953 | 2953 | 2953 |  | 
C2H6O | 46.07 |  |  | 2.59 | 2.59 | 2.59 | 2.59 | 25890.9 | 25890.9 | 25888.3 | 25888.3 | 25888.3 | 25888.3 | 25888.3 | 25888.3 | 2.6 | 2.6 | 2.6 |  |  |  |  |  |  | 
Lubricant | NA |  |  |  |  |  |  |  |  |  |  |  | 23 | 23 | 23 |  |  |  |  |  |  |  |  | 23 | 23
Total (kg/hr) |  | 36018.8 | 36018.8 | 42408.3 | 42408.3 | 42408.3 | 42408.3 | 42408.3 | 42408.3 | 25888.9 | 25888.9 | 25888.9 | 25911.9 | 25911.9 | 25911.9 | 16519.4 | 6389.5 | 6389.5 | 10129.9 | 10129.9 | 2953.0 | 2953.0 | 2953.0 | 23.0 | 23.0
Temperature (◦C) |  | 25 | 27 | 58 | 118 | 194 | 320 | 325 | 130 | 102 | 35 | 35 | 35 | 35 | 35 | 212.7 | 192 | 192 | 244 | 160 | 98 | 320 | 98 | 25 | 25
Pressure (barg) |  | 1 | 38 | 38 | 37 | 36 | 35 | 35 | 34 | 34 | 33 | 17 | 17 | 17 | 17 | 35 | 35 | 38 | 36 | 35 | 3 | 2 | 1 | 1 | 17
Vapor Fraction |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
R-110
D-120/130
F-150 A/B/C
[1] AIChE , "2018 Student Design Competition," AIChe, 2018.
[2] "Nasdaq GlobeNewswire," Crystal Market Research, 30 Nov 2017. [Online]. [Accessed April 2018].
Chart: End of Year
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 22
i = 0 | 0 | -3.4533 | -7.674 | -5.3062 | -2.9385 | -0.57076 | 1.797 | 4.1647 | 6.5325 | 8.9002 | 11.2679 | 13.6357 | 16.0034 | 18.3711 | 20.7389 | 23.1066 | 25.4744 | 27.8421 | 30.2098 | 32.5776 | 34.9453 | 37.3131 | 39.6808
i =0.10 | 0 | -3.1394 | -6.6275 | -4.8486 | -3.2314 | -1.7612 | -0.4247 | 0.79032 | 1.8949 | 2.899 | 3.8119 | 4.6418 | 5.3962 | 6.0821 | 6.7056 | 7.2724 | 7.7877 | 8.2561 | 8.682 | 9.0691 | 9.4211 | 9.741 | 10.0319
i = 0.182 | 0 | -2.7135 | -5.3197 | -4.1708 | -3.2681 | -2.5588 | -2.0014 | -1.5634 | -1.2192 | -0.94878 | -0.73627 | -0.56928 | -0.43806 | -0.33495 | -0.25393 | -0.19026 | -0.14024 | -0.10093 | -0.070035 | -0.045762 | -0.026689 | -0.011701 | 7.6181e-05
0-line | 0 | 0