## Slide 1
Methodology
Programs Used:
    EPA’s Portfolio Manager – used for benchmarking building’s energy usage.
    UNH’s SIMAP (Sustainability Indicator Management and Analysis Program) – built for calculating GHG emissions for college campuses.
Process:
Obtain building utility data
Enter total energy data into SIMAP
Generate Town GHG report
Enter energy data into Portfolio Manager by building
Obtain waste and transportation data
Enter total waste and transportation data into SIMAP
Introduction:
GHG inventories track the carbon pollution produced by towns. Understanding where greenhouse gas emissions are produced allows targeting reductions and determining their effectiveness.
The Town has made two previous efforts:
    2010 - first benchmarking completed using Portfolio Manager. Since then, several building have been added or removed.
    2013 - first Town Energy Action Plan created. While some efforts have been completed, many energy savings remain untouched.
Objectives:
Update the energy use benchmarking of municipal facilities
Create a greenhouse gas emissions (GHG) inventory that identifies future actions
Preliminary Results
Data collection
Town Facilities Benchmarking and GHG Emissions Update
Andrea Mott, UNH Sustainability Fellow
Mentor: Rick Norris, Town of Groton, CT
Data is still being collected.
The following analysis are completed without Groton Public schools and municipal fleets information.
Town Energy Efforts
HPS Streetlights converted to LEDs
Solar Landfill Project in the works, aimed to produce 5 MW
Energy efficient building efforts made from 2013 Energy Action Plan, such as scheduling HVAC systems, installing LED lights, adding occupancy sensors, replacing old boilers, and adding pump VFDs.
Energy (70 buildings tracked!)
Public Schools
Town Offices
Police and Fire Stations
Wastewater Treatment Facility
Street and Traffic Lights
Parks and Recreational Facilities
Waste and Wastewater
Waste produced by municipality
Wastewater treated at the plant
Transportation
Municipal workers commute
Municipal fleet
Analyzed based on fiscal year to keep consistent with financial records
Picked FY17 since FY18 just ended and data is not all available yet
5% Reduction
Figure 2: Groton municipal building greenhouse gas emissions by sources collected so far, comparing FY 2014 and 2017. Note: this data does not include Groton Public Schools, since the propane and fuel oil is still being collected
Figure 1: Percentage of Groton’s municipal greenhouse gas emissions by town department during FY 2017. The total electricity usage is 26.3 GWh.
Chart: FY 2017 Municipal Building Electricity Usage by Department
| WWTP | Streetlights | Parks/Rec | Public Schools | Police/Fire | Town Offices
Electricity Usage (kWh) | 4177878.7 | 512403.1253 | 68586.8399 | 7959221.4856 | 967420.6 | 1693517.8
18.4 Passenger vehicles driven for one year
29.9 tons of waste recycled instead of landfilled
9.3 homes energy usage for a year
1.1 tanker trucks worth of gasoline
85.8 metric tons of CO2e saved a year – which is equal to:
Next Steps
Finish municipal data entry and complete GHG inventory report
Determine effectiveness of Town energy reduction efforts
Time permitting, determine community emissions
Make recommended actions based on analysis and current Town Municipal Energy Policy
Challenges and Questions
How does a municipality take advantage of reducing pollution from natural gas without getting “stuck” on it?
How does a municipality balance growth with environmental goals?
How does a municipality move beyond short-term paybacks to tackle the long-term problems?
Chart: Municipal Energy by Source
| Electricity | Natural Gas | Fuel Oil #2 | Propane
FY14 | 27322520.4 | 3238055.9 | 9500720.4 | 1102445.2
FY17 | 26326093.7 | 2567051.9 | 9646641.7 | 1580450.7
Figure 4: Groton municipal building energy by fuel source. The only building with natural gas is the library, and the 21% reduction in energy shows their energy saving efforts.
LED Streetlights reduced emissions by 67%!
In February and March 2017, all Town owned High Pressure Sodium (HPS) streetlights were replaced with LEDs. This results in an annual savings of 330 MWh and 85.8 metric tons of CO2e.
Figure 4: Streetlight energy usage over time. The average monthly average drops from 41.2 MW to 13.7 MW after February 2017.
Chart: Streetlights Energy Usage
| 41820 | 41851 | 41882 | 41912 | 41943 | 41973 | 42004 | 42035 | 42063 | 42094 | 42124 | 42155 | 42185 | 42216 | 42247 | 42277 | 42308 | 42338 | 42369 | 42400 | 42429 | 42460 | 42490 | 42521 | 42551 | 42582 | 42613 | 42643 | 42674 | 42704 | 42735 | 42766 | 42794 | 42825 | 42855 | 42886 | 42916 | 42947 | 42978 | 43008 | 43039 | 43069 | 43100 | 43131 | 43159 | 43190 | 43220
 | 31966.4 | 35568.5 | 39410.8 | 45724 | 48703 | 52515 | 51736 | 43538 | 43237 | 37010 | 33727 | 29962 | 31932 | 34943 | 39379 | 45768 | 47767 | 52350.6 | 53127.8 | 47500.9 | 44310.6 | 37412.5 | 33821 | 31643.5 | 32232.4 | 35792.3 | 39681.1 | 45694.9 | 48792.7 | 52625.7 | 49827 | 43728.5 | 43573.9 | 14832.4 | 13239.6 | 11108.6 | 10399 | 11574.8 | 12548.5 | 13897.2 | 15641.7 | 16223 | 17038.6 | 16519.7 | 14535.1 | 13418.2 | 11428.2
Chart: Municipal Operation Emissions
| 2014 | 2017
Stationary Fuels | 1012.02 | 986.53
Purchased Electricity | 2096.02 | 1927.19
Workers Commute | 658.55 | 669.11