## Slide 1
Examining the influence of land use and flow variability on
carbon emissions from headwater streams - H21K-1813
Andrew Robison*, Wilfred Wollheim, Bonnie Turek
University of New Hampshire *Contact email: andrew.robison@unh.edu
Rivers are most often sources of CO2 and CH4 to the atmosphere (Drake et al., 2017), yet we lack a robust understanding of what drives the spatial and temporal variability of these emissions (Kaushal et al., 2014).
We have begun monitoring CO2 and CH4 dynamics within the Plum Island Ecosystems LTER river networks using high frequency pCO2 sensors and bubble traps to address the question:
How do alterations in the hydrologic and nutrient regimes caused by urbanization alter CO2 and CH4 production and emissions within a river network?
The Plum Island Ecosystems LTER (PIE-LTER), located in northeastern Massachusetts, contains the Ipswich and Parker River watersheds. This study focuses on four headwater streams of contrasting land use: Cart Creek (CC), College Brook (CB), Dube Brook (DB), and Sawmill Brook (SB). The land use characteristics of these streams is displayed below.
In-stream pCO2 sensors (SIPCO2; Hunt et al., 2017) were deployed to examine the influence of land use, flow, nutrients, light, and temperature on CO2 dynamics. Key differences in diurnal, event, and longer-scale patterns have been observed.
pCO2 (ppm)
Q (L s-1)
Temp (oC)
Discharge events alter pCO2
Temperature affects longer-term variability
Hunt et al. 2017
Ebullitive, or bubble-mediated, fluxes of GHGs were monitored at CC and SB, with 12 bubble traps at each site. Significantly more CH4 was emitted at SB via ebullition, comparable to the average reported for fluvial systems (Stanley et al. 2016).
The resolution provided by pCO2 sensors is critical in identifying process controls, and some broad-scale patterns are emerging in our initial monitoring.
A strong hydrological influence on pCO2 is clear, particularly the relationship between emissions and flow. Incorporating gas exchange measurements will improve emission estimates across flow conditions and sites.
Ebullition of CH4 is a major pathway of GHG emission. Constraining the spatial variability of ebullitive fluxes will be key to scaling to the reach and network scale.
This work will help in constraining the carbon balance of aquatic systems within a land use context.
Impervious Surface
Parker River
watershed
Ipswich River
watershed
Stream | Area (km2) | % Forest | % Developed | % Wetland | Ebullition monitoring
CC | 4.64 | 77.2 | 10.4 | 19.2 | Yes
CB | 3.03 | 11.8 | 64.6 | 1.3 | 
DB | 3.32 | 55.3 | 8.2 | 9.1 | 
SB | 4.01 | 10.6 | 88.3 | 4.1 | Yes
Motivation
Urbanization in the Watershed
High-Frequency pCO2 Sensors
Ebullitive Fluxes Significant for CH4
Discussion
Hysteresis and Flux Estimates
pCO2 (ppm)
Forested site with open canopy (DB) displays stronger diurnal signal
Forested site with closed canopy (CC)
05-Sep
13-Sep
09-Sep
Variable | Coefficient of determination (r2) | Comparative dimension
Sediment % organic | 0.25 | Spatial
Sediment % silt/clay | 0.00 | 
Canopy cover | 0.00 | 
Depth | 0.22 | 
Mean Q | 0.50 | Temporal
Mean temperature | 0.41 | 
Minimum barometric pressure | 0.30 | 
Butman, D., & Raymond, P.A. (2011). Nature Geoscience, 4(12), 839–842.
Drake, T.W., Raymond, P.A., & Spencer, R.G.M. (2017). Limnology and Oceanography Letters, 3(3), 132-142.
Hunt, C.W., Snyder, L., Salisbury, J.E., Vandemark, D., & McDowell, W.H. (2017). Limnology and Oceanography: Methods, 15(3) 291-301.
Kaushal, S.S., et al. (2014). Journal of the American Water Resources Association, 50(3), 585–614.
Stanley, E.H., et al. (2016). Ecological Monographs, 86(2), 146–171.
Vaughan, M.C.H., et al. (2017). Water Resources Research, 53(7), 5345–5363.
References
CC
SB
Totals
CH4 Flux via Ebullition (mmol m-2 day-1)
20
30
10
0
 | CC | SB
Mean | 0.35 | 1.87
Median | 0.02 | 0.17
Max | 3.61 | 25.6
Characteristics of hystere-sis (Vaughan et al., 2017), are variable across sites and individual storms (left). Despite these differences, evasion of CO2 is dominated by efflux during higher flow periods (below).
Flushing, clockwise
Diluting,
counterclockwise
Flushing, counterclockwise
CC
DB
SB
CB
10-Sep
11-Sep
12-Sep
pCO2 (ppm)
Discharge (L s-1)
Est. CO2 evasion rate (g m-2 hr-1)
4800
2400
0
1500
750
0
2
1
0
27-Aug
10-Sep
03-Sep
Diluting, counterclockwise
The estimated mean evasion rate at SB was 4.5 g C m-2 d-1, compared to the 6.5 g C m-2 d-1 reported by Butman and Raymond (2011) for streams in the U.S.