## Slide 1
Underwater Remotely Operated Vehicle (ROV)
Team members: River Iannaccone, Julie Berberian, Katherine Hernandez, Jennifer Conyers,
Ryan Kelly, Trevor Lounsbury, Mark Torpey
Project Advisors: Dr. May-Win Thein, Allisa Dalpe, Alex Cook, Ozzy Oruc
Underwater GPS
Goal: To locate the ROV underwater using four receivers listening for a set acoustic frequency and a single locater producing a desired acoustic frequency
Deployment
Goal: To autonomously deploy the ROV from the ASV
Strategy consists of custom built tether reel and tether stabilizers to control the deployment process
Tether reel has been fabricated out of
a 2000 pound winch motor, a cable
reel, and a slip ring
12 wire slip ring enables the
connection between the ROV, the
tether reel, and the ASV
Stabilizers are a mechanical system
that keeps the tether from snagging
on the ASV
UNH ROV Mission
The Remotely Operated Vehicle (ROV) in conjunction with the Autonomous Surface Vehicle (ASV) is aimed to complete a joint mission of ocean mapping. This mission focus is to accomplish being autonomously controlled to identify objects of interest.
Special thanks to Dr. Martin Renken, Scott Campbell, John Ahern, the CEPS Office of the Dean, and the Parent’s Association
Interchangeable Tether System
Goal: To make one tether system that will work with all current and future ROVs
Each ROV will have a female SubConn
connector and tethers will have a male
SubConn connector
ROVs can switch between
tethers
Connections can be inline (ROV 008)
or on the end cap (ROV 006 & 007)
ROV Autonomy
Goal: Having our ROV travel from an initial starting point and travel to a designated destination
Using Direct Feedback from MavLink and our underwater GPS we are able to analyze and control our ROV’s position.
Controls
Electronics
Redesign of ROV 007 electronics, converted electronics from a stack design to a modular tray design
Gathered data pertaining to power draw of the system to understand battery life
- The goal was to determine average power draw in an attempt to m increase overall run time
Confronted issue with inertial measurement unit (IMU) placement due to ROV 007’s rotating design
- Stationary tubes were installed on the side of the ROV to house m the IMU and camera
Sonar
Goal: to detect objects of interest on the seafloor surface
Blue Robotics "Ping Sonar Altimeter and Echosounder"
Benefits of this system include open source code, easy implementation with existing system, reasonably priced,
and the user interface displays data in an
effective manner
Drag Study
Goal: Determine a drag coefficient of ROV 008 to assist with creating a non-linear control model of the vehicle
Used the drag tank to drag the ROV
at varying velocities collecting drag data
Designed and fabricated an attachment
system so that the ROV could be secured
to the drag carriage
Collected Pylon data so that it can be
removed when dragging the ROV to isolate
the vehicle
Processed the drag data, re-arranging the
drag equation to determine the drag
coefficient
Estimated the Reynolds number and
plotted with the drag coefficient to
determine flow state
The figure above illustrates the drag on the ROV with respect to velocity.
Tether Deployment Torque Analysis
Goal: To control the deployment rate
The system will be analyzed from both analytically and experimentally.
The figure above shows simulated single beam sonar data.
The table above shows the system capabilities for the sonar.
The figure above shows the ROV deployment system from the ASV. It is important to note that tether reel is shown in blue.
The figure above shows the tether connected to ROV 007.
Fdrag = Cd ρ V2 A/2
Where:
: coefficient of drag
ρ: density of fluid
V: velocity of ROV
A: cross-sectional area
Measurable Distance | 30 meters
Depth Rating | 300 meters
Beam Width | 30°
WaterLinked Underwater GPS
Ability to change frequencies if noise levels are too great improves accuracy in a majority of environments
Accuracy varies at +/- 1% of the distance between the Locator and the Receivers
Using the underwater GPS along with controls developed, we are able to have the ROV travel autonomously from a starting location to a desired point of interest
Currently using the QGroundControl system we are able to manually select a point of interest and begin travel
The figure above shows the WaterLinked Underwater GPS MavLink.
ROV 007
ROV 008