## Slide 1
Lonza Biologics Campus Expansion, Portsmouth, NH
Allan Masison, Nicholas Francis, Owen Sweet, Philip McHenry (PM) & Rezwan Ali
Project Advisor: Anthony Puntin, P.E. | Project Sponsor: Patrick Crimmins, P.E.
Scope of Work
40+ boring logs were provided
Refusal typically between 12-18 ft
Mostly fill, dense silty clay and dense sand layers
Frost line 3 feet below grade
Shallow foundations
Program
  Merge Iron Parcel with existing campus to provide cohesion
  3 phases for development
  1-million ft2 of industrial space
  1,000 future employees
  Minimum 667 parking spaces
  Minimize environmental impact
  Daylight Hodgson Brook
Existing Conditions
  23-acre site, the “Iron Parcel”
  Neighboring Lonza facilities
  Hodgson Brook flows under site in 48-inch concrete pipe
  1.73 acres of wetland area
  Large soil pile
  Chlordane contamination
  Historically served as housing for Pease Air Force Base
Stream Restoration
Chart: Proposed Elevation Profile
| 0 | 360 | 720 | 1080 | 1440
Elevation Station (ft) | 56 | 50 | 44 | 41 | 38
Stormwater Management
  Subsurface gravel wetland for Phase 1
  Water Quality Volume (WQV) = 15,000 ft3 , 1-inch storm
  95% theoretical removal efficiency
Foundations
  Conceptual master plan for proposed campus expansion
    Building locations
    Traffic circulation
    Parking
  Stream restoration design
  Foundation & pavement recommendations
  LID stormwater management
  Environmental assessment
Pavement
  2-year flow = 52.1 cfs ; 100-year flow = 175.9 cfs
  Drainage area = 131.8 acres
Acknowledgements
Wetland Impacts
  Mitigation is required by law when wetlands are impacted (NHDES)
  1.73 acres of wetlands; 0.93 acres impacted, 0.80 acres avoided
  $200k expected contribution to the Aquatic Resource Management (ARM) Fund for wetland impacts
  Special thanks to our sponsor, Patrick Crimmins from Tighe & Bond, our advisor, Anthony Puntin, and the help provided by Joel Ballestero, Prof. Tom Ballestero, Prof. Jo Sias, and the UNH Stormwater Center.
(3D perspective)
3