## Slide 1
High Speed Cavitation Tunnel (HiCaT) Restoration
Chris Robb, Davis Cole, Matthew Carey
Advisors: Ivaylo Nedyalkov, Martin Wosnik
Assembly
General Techniques
Align Sections
New O-rings
Vacuum grease
Gaskets as necessary
RTV to seal smaller fittings
Proper fastener sizes and torques
Issues
Alignment
Leg length differences
Leakages
Galvanized parts needed trimming
Impeller & motor alignment
Driveshaft seals
Honeycomb
Axisymmetric Test Bed
Electrical & Instruments
Future Work
Pressure System
2 Honeycombs installed between riser tank and test section
≈14” after each honeycomb for turbulence decay (minimum was 10”)
4 Brackets per honeycomb
Minimal Flow Interference
≈100 lbf per honeycomb at max operating speed (25 lbf per bracket)
Objectives
Assemble and seal all pieces
Operating envelope of 0.5-2 atm & 180-1770 RPM (≈1.7-16 m/s)
Design, build, & test axisymmetric test bed
Performance Flow Measurements
Calibration of RPM and Test Section Velocity
Write Operating Manual
Currently can test wingtips & foils
Testing water flows around axisymmetric bodies
Fits existing instruments and openings
Pressure taps for measuring pressure distribution in cavity
Pressure taps for changing cavity pressure
Less than 4% blockage of test section
Applications for design of high-speed underwater vehicles
Pressure calibration of motor RPM and test section velocity is ongoing
HiCaT Operating Manual is in draft stages
Validate Calibration results with Particle Tracking Velocimetry
Determine velocity profile in test section using Laser Doppler Velocimetry & Particle Image Velocimetry
Test axisymmetric test bed
Independent pressure control of tunnel
New pressure fittings and vacuum rated tubing
New quick connect fittings
Test section pressure maintained electronically with control valves
Separate access to pressure and vacuum for manipulating cavity pressures
Motor & Motor Controller wired
Emergency Stop added
Operating Instrumentation mounted, plumbed, & wired
All wiring waterproof below 4’ height & routed cleanly back to workstation
Motor and pressure valves controllable from workstation
16 Predefined motor speeds, or analog control
Before
After