## Slide 1
HEAT EXCHANGER COMPARISION
KEVIN ADAIR, KYLE YORK, ALI ASGHAR. University of New Hampshire
Introduction
Objectives
Methods
Results
Conclusions
References
Three heat exchangers were tested (double tube, shell and tube and plate) for:
Different cooling flow rates
Different flow patterns (Co-Current/Counter-Current)
The trend for overall heat cofficents as changes are made
The average heat coefficients using a wilson plot analysis (Fig.5)
Design Problem:
Reactant stream 180 lpm
Heated from 20°C to 50°C
Heating medium is water at 80°C
Wilson plot determine the average heat transfer coefficients for the Double Tube heat exchanger
Most efficient design problem solution was determined based on spatial efficacy:
Counter-current plate heat exchanger
  Total heat transfer area is 158 m²
  Total width of plates should be 4.5 m
  Can be split up into parallel systems
  Total system plate length should be 35.1m
Proposed Solution:
  Three systems in Parallel
  Each System has 9 plates
  Each plate is 4.095m x 1.550m
  Total Heat exchange area 171m²
Hot water flow and temperature kept constant at 2.0 l/min and 40°C
Cold water flow varied at 0.5, 1.0, 2.0 and 3.0 l/min.
3 different heat exchangers were tested
Each test conducted in triplicate for the given cold water flow rates
each heat exchanger was also tested for the different flow patterns (Co-current/Counter-Current
Data was recorded for the cold water flow rates, Temperatures of cold and hot water in and temperatures of cold and hot water out.
Heat exchangers are used to transfer heat between fluids. There are different types of heat exchangers that work in various ways. Each heat exchanger has a different heat transfer coefficient that relates to it and the conditions applied to it.
The heat transfer coefficient for the double tube exchanger is shown to be larger with co-current occuring, as flow increased the coefficient in both trends increased with similar rates.
The heat transfer coefficient for the shell and tube is larger under co-current at smaller flow rates while the opposite is true at higher flow rates.
Geankoplis, C. J. (1978). Transport processes and unit operations. Boston: Allyn and Bacon.
Heat transfer coefficient for the plate exchanger is larger under countercurrent at smaller flow rates while the opposite is true at higher flow rates.
Cruithne9 (https://commons.wikimedia.org/wiki/File:Comparison_of_con-_and_counter-current_flow_exchange.jpg), https://creativecommons.org/licenses/by-sa/4.0/legalcode, accessed 26 April 2019
Water Heater
Cold Water Flow Control
Cold water Inlet
Hot Water inlet
Hot Water Outlet
Shell and Tube Exchanger
Plate Exchanger
Double Pipe Exchanger
Hot Water Gear Pump
J. F. Zhou, Y. Li, B. Q. Gu and C. L. Shao, Figure 1, Temperature Field Prediction of Rectangular Shell-and-Tube Heat Exchanger, 10 December 2011
Industmarine Engineers, www.industmarine.com/content/essentials/plate-heat-exchanger.php, accessed 30 April 2019
Meenu Jain Lalitpur, Double Pipe Heat Exchanger Animation, https://www.youtube.com/watch?v=MdDbxktvecg, accessed 30 April 2019