## Slide 1: Autonomous Surface Vehicle (ASV)
Team Members: Ian Lander, John Ross, Hunter Miller, Kevin Johnson, Trevor Lounsbury, Nicholas Arnold & Allisa Dalpe
Project Advisors: Dr. May-Win Thein & Dr. Yuri Rzhanov
Graduate Advisors: Allisa Dalpe, Alexander Cook, & Oguzhan Oruc
In collaboration with the UNH Remotely Operated Vehicle (ROV) project
Special Thanks to Dr. Martin Renken, the UNH Parents Association, John Ahern, Scott Campbell, Laura Gustafson, Sheri Millette & Tate Ellinwood (St. Paul’s School)
ROS UML
Electronics Overview
Transitioning from MOOS-IvP® to ROS ®
TUPPS (TESTING UNMANNED PERFORMANCE PLATFORMS)
Mission
The ultimate goal of this project is to have autonomous ASV and ROV deployment, which is also able to behave as a swarm with other ASV and ROV pairings. The intended application of this system is autonomous sea floor mapping.
The goals for this summer include finalizing deployment of the ROV and Underwater GPS systems, as well as achieving waypoint-to-waypoint navigation and integration of the ROS platform.
Purpose: A small-scale version of the ASV for indoor testing in a tank.
Cost-effective construction
Modularity with structural parts
Arduino, Raspberry Pi, and other open-source components
Ultrasonic sensor for obstacle detection
Adjustable PVC sensor housing
Acoustic sensors do not function optimally in a tank
  Signals reflecting off of walls interferes with data collection
  Necessary to test sensors in relatively still, but open water
Tank is too small to test ASV autonomy, and GPS does not work inside
  Necessary to test autonomy in lake
ASV Lake Testing
waterline
Standard laptop
  Sensor data processing
  Navigation commands
  Shore-to-vehicle communications
  Vehicle-to-vehicle communications
Arduino Mega 2560 (x2)
  UGPS Deployment
  ROV Deployment
  Propulsion Control
ASV has ‘front seat’ controller and ‘back seat’ communication hub & mission manager
Front seat is an Arduino Mega2560 board using Robot Operating System (ROS) serial communication to engage with back seat
  ROS is a node-based, platform-agnostic communication framework
Back seat is a computer running Linux (Ubuntu)
  Runs master roscore instance
  Communicates with shore station or the ROV
Underwater GPS Deployment
The Waterlinked® Underwater GPS© System (UGPS) Components
  4 submersible transducers (on ASV)
  1 receiver (on ROV)
  Electronics dry box (on ASV deck)
Employs a low-power linear conveyor to deploy the transducers to their operating depth of 1m
System stabilizes the transducers
  Allows for precise location monitoring of the ROV
Detachable for transportation of ASV
Uses a global and local planning hybrid structure
  Accounts for prior knowledge of an area
  Accounts for newly detected obstacles real time
Layered strategy using multiple vector fields
  Basis of vector field generation comes from the Potential Field Method (PFM)
  Fields can be added or removed for mission specific needs
  Can account for environmental factors (i.e. wind, waves, currents)
  A* / PFM acts as global planner, PFM alone is the local update
Fields added together using vector summation
Path Planning
Simulated A*/PFM route plan in Portsmouth Harbor (Portsmouth, NH)
Visualization of multiple vector fields
Potential Field Method equations
UML based design for ROS infrastructure allows for modularity between existing systems and implementation of new devices.
Le Guevel, Sonia. “Thales Wins French-UK Mine Countermeasures Contract.” Thales Group, 2019 Thales Group, 27 Mar. 2015, www.thalesgroup.com/en/worldwide/press-release/thales-wins french-uk-mine-countermeasures-contract.
Notes: To change this poster, replace our sample content with your own. Or, if you'd rather start from a clean slate, use the New Slide button on the Home tab to insert a new page, then enter your text and content in the empty placeholders. If you need more placeholders for titles, subtitles or body text, copy any of the existing placeholders, then drag the new one into place.