## Slide 1
Municipal Greenhouse Gas Inventory Lebanon, NH
Cassidy Yates, UNH Sustainability Fellow, Summer 2019
Mentors: Mark Goodwin & Rebecca Owens, City of Lebanon
Overview
The City of Lebanon, NH has set goals for improving energy efficiency, implementing renewable energy, and reducing their greenhouse gas (GHG) emissions by 80% below 1990 levels by 2050
A GHG inventory measures progress and supports further planning, resource allocation, and policy development
To evaluate progress and re-examine priority areas, updated inventories were completed for 2015 and 2018
Emissions Summary Table
Emissions by Percent
Emissions Reduction Scenarios
Approach
Local Government Operations Inventory
Program Used: EPA Local GHG Inventory Tool
Inventory Process
Data collection
Program research
Data organization
Data input
Data included:
Preliminary Results
10,938 MTCO2e were emitted in 2018, a 33% reduction from 2015
The overall reduction is largely due to a 44% reduction in landfill emissions since improving the landfill gas collection system
Landfill emissions account for 66% of the total emission for 2018
Fleet vehicle emissions increased by 10% from 2015 to 2018
A forest half the City’s size is needed to sequester it
10,938 metric tons of carbon dioxide equivalent were emitted by Lebanon Municipal Operations in 2018
Chart: 
| Landfill | Fleet | Electricity | Heating Fuel | Employee Commute | Streetlights | Business Travel
2018 | 0.65545 | 0.10578 | 0.094112 | 0.094895 | 0.039265 | 0.0093976 | 0.0010971
Landfill
Fleet Vehicles
Heating Fuel
Electricity
Employee Commute
Streetlights
Business Travel
Analysis
Review
Report
Chart: Emissions (MTCO2e)
| 2015 | 2018 | LED Streetlights & Solar Phase 1 | LED Streetlights, Solar, LFG to Energy | Goal
Landfill | 12711.72 | 7169.27 | 7169 | 7169
Fleet | 1050 | 1157 | 1157 | 1157
Electricity | 1096.96 | 1029.38 | 798 | 0
Heating Fuel | 1022.42 | 1037.95 | 1038 | 1038
Employee Commute | 420.01 | 429.47 | 429 | 429
Streetlights | 109.02 | 102.79 | 38 | 38
Business Travel | 17 | 12 | 12 | 12
Entire | 0 | 0 | 0 | 0 | 3285.4
-33%
-35%
-40%
-80%
Discussion
2009 baseline used to compare emissions for heating fuel and electricity for some buildings
3 major projects are currently in place to further reduce emissions to 40%
Next steps: Improve data collection, measure more emissions sources, conduct a community wide inventory