## Slide 1
Understanding the effects of impoundments on river network nitrogen removal
Christopher Whitney*, Wilfred Wollheim
University of New Hampshire, Department of Natural Resources and the Environment
*chris.whitney@unh.edu
Background
Reach-scale N fluxes are altered by impoundments
Unmet N demand downstream can buffer against increased exports from river networks after dam removals
Study Area & Methods
Dam removals will lead to greater reach-scale N exports
Conclusions
Across the US, human-made dams are being removed due to safety concerns as well as to restore rivers to more natural flow and sediment regimes
However, the undamming of rivers may have substantial effects on nitrogen exports to coastal areas.
With the removal of impounded water bodies, there will be a decrease in water residence times, interception of incoming nutrient loads, and shifts in dominant biogeochemical processes
However, over the last 20 years there has also been an increase in the number of beaver impoundments, potentially leading to opposite effects as human dam removals
This shift in human to beaver-dominated impoundments will result in alterations to the form and timing of nitrogen exports from basin mouths, affecting the watershed response to changing climate and land use
Impoundments are effective reach-scale transformers of N species but dominant biogeochemical processes differ between human and beaver impoundments leading to differences in N exports
Removal of human dams will result in increased reach-scale N exports
River networks with greater impounded surface area are able to retain higher proportions of N
Unmet N demand in river networks downstream of human-made impoundments will attenuate additional N fluxes following dam removals
Acknowledgements
Plum Island Ecosystems LTER (OCE–1238281 and 1637630)
EPA STAR Graduate Research Fellowship (FP-917819)
Impoundments within river networks are effective at removing N
 | DIN (kg yr-1) | DON (kg yr-1) | PN (kg yr-1) | TN (kg yr-1)
2016 | +290.0 | -136.1 | -30.7 | +123.3
2017 | +477.3 | -216.8 | -47.5 | +212.9
Increase
Decrease
N fluxes after removal of the human reservoir were modeled using the N removal vs. hydraulic load empirical relationships (above) and assumed an increase in hydraulic load from decreased surface area after the dam removal.
Estimate the abundance and distribution of beaver ponds in the PIE watersheds since pre-expansion to present day
Derive separate functions for loading, removal and transformations of all N species using field data to better understand river network-scale effects of impoundments on complete N cycle
Use abundance and distribution of beaver ponds through time with dynamics of all N species in a spatially distributed model to understand changes in N exports through time and make predictions of future change
Next Steps
-9.7%
-20.2%
-31.7%
-2.9%
-5.9%
-9.3%
River networks without beaver ponds have greater DIN exports than those with following dam removals
River networks with beaver ponds have lower post-dam removal DIN exports
Removal of the dam will result in an increase in DIN fluxes and an increase in DON & PN fluxes with the net effect being a slight increase in total N
Human reservoirs tend to decrease DIN loads due to high NO3 retention. This beaver pond is a DIN source due to production of NH4 which is possibly due to low N inputs from upstream beaver ponds
River networks as a whole are efficient at removing DIN, with greater removal occurring with increasing impounded area.
Addition of beaver ponds has greater impact on DIN removal compared to human reservoirs.
Removal is greater at lower annual discharge.
Four impoundments (3 human, 1 beaver) within the PIE LTER currently being monitored on a monthly basis
Intensive monitoring of one human reservoir currently scheduled for removal (SMD) and one mature beaver pond (CCBP)
Mass balance of different forms of nitrogen (N) species: dissolved inorganic (DIN) & organic (DON) and particulate organic N (PN) estimated via grab samples collected at inflows and outflows of impoundments
River network-scale modeling of DIN fluxes to examine how changes in impoundment numbers affect N exports to the coast
Human Reservoir
Beaver Pond
3 human reservoirs on mainstem
Assume 0.8 beaver ponds/km throughout entire network (PIE LTER unpub. data)
Assumes beaver pond area changes as a function of stream order and size of channel being replaced by pond
Assumptions will be tested with further measurements