## Slide 1
Core Handling for the South Pole Ice Core (SPICEcore) Project
FIGURE 2. Panel A shows the layout for the drilling and core processing operations. Panels B shows the inside of the underground core storage trench and the lift system used to transfer the packed ice core boxes to the surface. The trench served as a storage area for all of the drilled ice until it was ready to be flown from South Pole Station to McMurdo Station. In addition, all of the ice from the ‘brittle ice zone’ was stored in the trench over winter to provide more time to relax internal stresses before the ice was shipped back to the U.S. Panel C shows the surface operations as an ice core box is lifted out of the underground storage trench. Panel D shows a SOLIDWORKS rendering of the core handling system. Panel E and F show the inside of the drilling tent. The U.S. Ice Drilling Program group at the University of Wisconsin-Madison designed and built the drilling system, called the Intermediate Depth Drill (IDD), and core handling system. Based on the Danish Hans-Tausen Drill (Johnson et al., Annals Glac. 2014), the IDD was purpose-built for coring 1,500+ meters of ice.
B
E
F
http://spicecore.org
Joseph M. Souney1, Murat Aydin2, T. J. Fudge3, Jay A. Johnson4, Tanner W. Kuhl4, Eric J. Steig3, and Mark S. Twickler1
1Univ. of New Hampshire, Durham, NH, United States 2Univ. of California Irvine, Irvine, CA, United States 3Univ. of Washington, Seattle, WA, United States 4Univ. of Wisconsin, Madison, WI, United States
The stable isotope, aerosol, and atmospheric gas records in ice cores provide exceptional archives of past climate. Supported by the U.S. National Science Foundation (Office of Polar Programs – Antarctic Glaciology), a new 1,751-meter long ice core (~54,000 years in age) was recovered from South Pole, Antarctica, during the 2014-2015 (0 to 736 m) and 2015-2016 (736 to 1751 m) field seasons using the new U.S. Intermediate Depth Drill. Ice from the brittle ice zone was left at the site to relax. A third field season was required to pack and ship the brittle ice from the second field season back to the USA, although in hindsight the ice was not brittle. Very few measurements were performed on the ice in the field. The primary goal of the on-site core handling was to remove as much of the Estisol-140 drill fluid from the core as possible, assign a precise depth to the ice, and safely prepare the ice for transport back to the NSF Ice Core Facility in Denver, Colorado, USA, for subsequent intensive processing and sampling.
ABSTRACT
LOCATION
FIGURE 1. Top: South Pole drill site (SP, red circle). The drill site is approximately 2.7 km from South Pole Station. Middle: Aerial view of the drill site. The drilling took place inside the long red and white tent. Bottom: General characteristics of the drill site location.
Latitude | 89°59’ 20.168” S
Longitude | 98°09’ 34.528” W
Altitude | 2835 m a.s.l.
Ice thickness | 2700 m
Accumulation rate | 8 cm w.e.a-1 (20 cm snow)
Ice velocity | 10 ma-1 along 40°W
Mean annual temperature | -49°C (-56°F)
15 m depth firn temperature | -51°C (-60°F)
CORE HANDLING PROCESS
FIELD LAYOUT
ACKNOWLEDGEMENTS
This work is supported by US National Science Foundation grants OPP-1142517 (Aydin), OPP-1141839 (Steig), OPP-1142646 (Twickler) and the NASA Cryospheric Sciences Program. We thank the U.S. Ice Drilling Program (IDP; OPP-1327315) for drilling the ice core; the National Science Foundation Ice Core Facility for curating the core; the Antarctic Support Contractor for logistics support in Antarctica; the 109th New York Air National Guard for airlift support; and CH2M HILL Polar Services for drill test support in Greenland. We appreciate the collaboration with the Centre for Ice and Climate, University of Copenhagen, Denmark, on the design of the U.S. Intermediate Depth Drill.
GENERALIZED CUT PLAN
98 mm
archive
gases
FIGURE 3. Generalized cut plan of the 98 mm diameter SPC14 ice core.
The ice core was cut and sampled at the National Science Foundation Ice Core Facility in Lakewood, CO, during the summers of 2015, 2016, and 2017.
Over 10,300 samples have been cut to date from the ice core and sent to 14 individually NSF-funded institutions for analysis.
A: chemistry
B: continuous water isotopes
C: discrete water isotopes
D: Beryllium-10
A
B
C
D
D
C
REFERENCES
Johnson, JA, Shturmakov, TW Kuhl, N Mortensen, CJ Gibson. Next generation of an intermediate depth drill. Ann. Glaciol. 55(68), 27-33, 2014.
Hvidberg CS, Steffensen JP, Clausen HB, Shoji H, Kipfstuhl J. The NorthGRIP ice-core logging procedure: description and evaluation. Ann. Glaciol. 35, 5-8, 2002.
D
Receiving/Logging
Inside temperature between -20 to -25°C. Radiative heating in the tent.
Rigid tables with adjustable-height aluminum core tray rail system
2 m of ice received
Fluid evacuation device (FED) for removing drill fluid, followed by hand-vacuuming and towel-wiping
Brittle ice pushed directly into elastic netting (619 – 1078 m) **
Logging procedure based on NorthGRIP procedure (Hvidberg et al., Annals Glac. 2002)
** The length is measured, the ends tagged, and the 2-meter-long run of ice is pushed into a cardboard tube and set to rest on the racks in the core storage trench. The ice winters-over and is cut into 1-meter-long sections the following season.
Cutting
2 m drill runs cut into 1 m sections
Circular saw w/ tungsten carbide tipped 14” blade
Packing
1 m cores into 6-mil layflat and then into Al-coated cardboard core tubes
4 core tubes (packed in snow)/ISC box; 8 ISC boxes/wood skid; 4 wood skids/Air Force Pallet (AFP)
Temperature loggers inside ISC boxes & on each skid
1”-thick, quilted insulated blanket under AFP netting
Storage
4.5 m (W) x 7.3 m (L) x ~2.74 m (H) core storage basement
Temperature varied between -30 to -35°C
Brittle ice allowed to relax over winter in basement
Served as storage area for packed ISC boxes
Mechanical lift system for moving packed ISC boxes out of storage and onto surface
Shipping
Palletized ISC boxes from South Pole to NSF Ice Core Facility (Lakewood, CO, USA)
Cold-deck LC-130 flights from South Pole to McMurdo Station
-30oC SAFECORE shipping containers w/ dual cooling & power systems
4.5m
(15’)
7.3m (24’)
shelving
ceiling
hatch
A
Underground core storage trench
2017
2015
2014
2013
2016
NSF-ICF CPL’s:
0-555
556-734
1078-1462
735-1077
1463-1751
South Pole drilling
operations:
drill to 1751m, begin packup
complete packup
install, drill
to 736m
South Pole ice
retrograde:
585-734
1078-1478
735-1077
1479-1751
0-584
TIMELINE