## Slide 1
Assessing Controls of Methane and Carbon Dioxide Emissions from a Temperate Reservoir
1Department of Biological Sciences, University of New Hampshire, Durham, USA, 2Department of Earth Sciences, University of New Hampshire, Durham, USA, 3Institute for the Study of Earth, Oceans, and Space, University of New Hampshire, Durham, USA, 4Department of Natural Resources, University of New Hampshire, Durham, USA
Angelica M. Dziurzynski1,2, Clarice R. Perryman2,3, Natalie A. White4, Ruth K. Varner2,3
B35E - 1472
Background:
Temperate inland waters are major sources of atmospheric CH4 and CO2 1,2
Increased climate warming will lead to increased CH4 and CO2 emissions as warming encourages microbial metabolism of organic carbon in lake sediments 3,4
Inland waters are projected to have increased productivity, leading to excess CH4 and CO2 emissions 5,6
Study Site:
The Old Durham Reservoir (ODR) is a 13 acre highly eutrophic inland water body located in Durham, NH, USA 7 (Fig. 1, 2)
Characterized by calm waters and is dominated by Nymphaea odorata
Methods:
Flux Measurements:
Deployed nine bubble traps to collect ebullitive CH4 emissions (Fig. 3 a,c)
Used three floating static flux chambers to measure net CH4 and CO2 approximately weekly (Fig. 3 b)
Sampled water temperature and pH at water surface and sediment surface
Collected surface water samples to be analyzed for dissolved CH4 and CO2, DOC, TDN, and other water quality parameters
Drone Imagery:
UAV was flown over reservoir on July 8th, 2021
Captured multispectral images
Analyzed images using QGIS
Georeferenced bathymetry map to scale ebullitive fluxes 8
Trace Gas Analysis:
Samples were analyzed for CH4 using a GC-FID and for CO2 using an IRGA
Data was analyzed using R-coding and Excel
Research Questions:
What is the magnitude of ebullitive CH4 emissions across the reservoir with variable depth?
How do net CH4 and CO2 emissions from the reservoir vary with depth?
Fig. 2 Dominant vegetation at ODR (Nymphaea odorata, American water lily)
Results:
Fig. 6. Depth (ft) gradient of ODR (a) and ebullitive CH4 emissions (mg m-2 d-1) scaled by depth (b). ODR drone imagery was georeferenced to a previously made bathymetry map of the reservoir. Polygons were created to signify depth variation. Extrapolated ebullitive CH4 data (y = 263.04e-0.631x) from Fig. 5 was used to scale emissions across the reservoir.
Fig. 3. Bubble trap before deployment (a). Floating static flux chamber (b). Bubble trap deployed at ODR (c).
Acknowledgements:
This work was supported by the Hamel Center for Undergraduate Research through the University of New Hampshire. Thank you to the UNH Trace Gas Biogeochemistry Laboratory for the use of their facilities. Special thanks to Dr. Michael Palace, Dr. Sophie Burke, and Mr. Franklin Sullivan for the drone imagery and QGIS assistance. Special thanks to Mr. Owen Price for his endless support. Thanks to Ms. Cynthia Bova for collecting additional samples.
Conclusions:
Average net CH4 emissions were strongly associated with depth, whereas average net CO2 emissions were not (Fig. 4)
Ebullitive CH4 emissions varied with depth, and when scaled, the ebullitive CH4 budget for the reservoir was 1.0 kg d-1 (Fig. 5, 6b)
Differences in CH4 and CO2 fluxes between shallow, middle, and deep sites may also be impacted by differences in vegetation cover (Table. 1), as emergent and floating aquatic vegetation can impact carbon inputs, microbial activity, and gas transport in freshwater ecosystems
As the climate continues to warm, temperatures will increase and lead to further primary productivity and nutrient availability, which will contribute to increased CH4 and CO2 emissions
Future studies can be done to determine seasonal changes in CH4 and CO2 emissions from ODR
Fig. 1. Aerial image of ODR taken on July 8th using UAS. Image courtesy of Michael Palace and Franklin Sullivan (palace@guero.sr.unh.edu) and geology.com.
(a)
(b)
(c)
References:
1Bastviken et al. (2011), Science.; 2Raymond et al. (2013), Nature.; 3Audet et al. (2017), Freshwater Biology.; 4Marotta et al. (2014), Nature Climate Change.; 5Beaulieu et al. (2019), Nature Communications.; 6Wik et al. (2013), Journal of Geophysical Research.; 7Blanchette and Haney (2002), Center for Freshwater Biology. 8”Durham Reservoir Depth Map,” <https://usa.fishermap.org/depth-map/durham-reservoir-nh/#top-content>.
Net CO2 Flux (µmol m-2 s-1)
Net CH4 Flux (mg m-2 d-1)
Ebullitive CH4 (mg m-2 d-1)
n = 12
n = 12
n = 12
n = 12
n = 12
n = 12
n = 12
n = 3
n = 12
Fig. 5. Average ebullitive CH4 (mg m-2 d-1) collected from floating bubble traps compared to depth sites. Samples (total number = n) were collected from June 21st through October 22nd, 2021. Note: trap SB broke on July 8th, which resulted in 3 samples being taken. Ebullitive CH4 was extrapolated to modal emissions by depth using an exponential fit (y = 263.04e-0.631x) with R2 = 0.8135.
Depth | DOC (mg C/L) | TDN (mg N/L) | NO3 (mg N/L) | Surface Temperature (°C) | Bottom Temperature (°C) | Surface pH | Bottom pH | Lilypad % Cover
Shallow | 20.7 ± 5.0 | 0.76 ± 0.2 | 0.0091 ± 0.002 | 24.4 ± 3.8 | 20.8 ± 3.3 | 5.8 ± 0.4 | 5.3 ± 0.3 | 51.2
Middle | 19.7 ± 4.2 | 0.70 ± 0.1 | 0.0088 ± 0.002 | 23.7 ± 4.5 | 19.3 ± 2.1 | 5.7 ± 0.4 | 5.3 ± 0.4 | 16.1
Deep | 17.7 ± 4.5 | 0.69 ± 0.1 | 0.0089 ± 0.003 | 22.8 ± 4.3 | 18.8 ± 1.9 | 5.9 ± 0.6 | 5.4 ± 0.4 | 20.6
Fig. 4. Average net CH4 fluxes (mg m-2 d-1) (a) and average net CO2 fluxes (µmol m-2 s-1) (b) compared to depth sites. Depths at sampling sites are 4.26 ft, 5.24 ft, and 7.54 ft at the shallow, middle, and deep sites, respectively.
Table. 1. Average water quality and temperature measurements and N. odorata percent coverage by depth site. DOC, TDN, and NO3 were measured from surface water samples.
(a)
-2 -1
(b)
(a)
(b)