## Slide 1: Marine And Naval Technological Advancements for Robotic AutonomY (MANTA RAY): Autonomous Surface Vehicle (ASV), and Unpiloted Underwater Vehicle (UUV)
TESTING unpiloted
PERFORMANCE PLATFORM (TUPPS)
Future Plans
Background
Testing
Manta Ray Mission
Tether Tensioning System (TTS)
PI: Dr. May-Win Thein CO-PI: Dr. Yuri Rzhanov
Graduate Advisors: Nick Custer, Richard Randall, Oguzhan Oruc, Hannah Arnholt, Igor Vladimirov
Team Members: Matthew Radzelovage (ME), Jenna Ehnot (OE), Jessica Barker (ME), William Seguin (ME), Patrick McKinnon (CS), Andrew Weeks (CS), Marguerite Kennish (ME), Jack Hamilton (ME), Brendan Ulrich (ME), Noah Wilder (CS),
Jeff Pitts (CS), Sydney Chock (EE), Gabriella Liano (EE), Aidan Boucher (CS)
Several full-scale tank tests were performed in the Chase engineering tank to test the subsystems and autonomous launch protocol
Acoustic modems, “Indoor GPS”, were used to simulate GPS waypoints for the Pixhawk flight controller
Our findings show that the final design is ready for more robust components and wiring
Needed to track the UUV’s position with respect to ASV location
Uses a Waterlinked® Underwater SBL© System
  4 submersible transducers (on ASV), 1 receiver (on UUV), and an Electronics dry box (on ASV penthouse)
Updated old linear arm system to cascading arm system
  Submerges acoustic transducer further underwater, thus increasing accuracy
  Faster deployment time
  Sturdier, less upkeep
Each arm utilizes a bi-directional spooling method in conjunction with dual limit switches to deploy and retract the nodes
UGPS API interface to retrieve GPS coordinates for UUV
Mission assertation for UUV from ASV
Reorganize the subsystem code
UUV Retrieval sequence
Active spooling on TMS
Open water testing off UNH Research Pier in New Castle, NH
Rotary encoder added to allow for deployment/retrieval of tether based on distance, rather than time
Three pully system with motorized rubber compliant wheel that spins at the same rate as the tether deployment motor, applies tension to tether and prevents back spooling at the winch
Winch axle rewelded to be aligned with motor gearbox
Cascading Arm SOLIDWORKS Rendering
Retracted
Deployed
Mechanical Design
Catamaran: 7’9” length, 5’6” beam
Twin 55lb thrust electric trolling motors
Winch and trapdoor for UUV tether management and deployment
Customized skid for the UUV control hardware and future sensor housing
UGPS acoustic node deployment
Software Design
Pixhawk Flight Controller
Hardware for open-source autopilot
Enables missions uploads and performs scripted autonomous navigation between waypoints, as well as remote-controlled capabilities
Contains a robust sensor suite including a compass, internal IMU, and GPS capability
Robotic Operating System (ROS)
Open-source robotics middleware suite
Enables communication between Pixhawk, ASV, and UUV subsystems through a network of publishers and subscribers
MavLink protocol
Communication between ASV & UUV
ASV controls the sequence of UUV operations by calling functions
Capabilities
  Tracking system location with GPS and acoustic system (UGPS)
Transmission hub for the system for data and updates to the shore station
Autonomous path planning and heading control
UUV deployment and retraction
UUV’s extrapolated underwater positional vector from acoustic relative position to known GPS coordinates on board ASV
Launch Protocol
Purpose: A reduced version of the ASV that replicates the full-scale ASV's architecture
Cost-effective, modular construction, ideal for indoor tank testing
Microcontroller simulates the ASV subsystems
Raspberry Pi ARM to replicate the ASV computer
Pixhawk flight controller
Pontoons redesigned with PVC pipe, 3D printed end caps and repositioned Blue Robotics thrusters
Waterlinked® Components
Team MANTA RAY is an interdisciplinary project dedicated to creating, maintaining, and expanding a network of marine robots for seafloor mapping and underwater perception. The network began as just the autonomous surface vehicle (ASV) and unpiloted underwater vehicle (UUV), but has expanded to include a prototype of the ASV, known as TUPPS, and two kinds of remotely operated vehicles, known as GUPPS and KRILL. With these systems, students work to improve communication between vehicles, develop autonomous behaviors and algorithms, and upgrade existing mechanical systems to improve precision and performance.
Uses ROS to allow communication between each subsystem on board to know when to deploy
Deployment.py listens to ROS topics that the Pixhawk publishes to allow detection of when the ASV has reached the desired waypoint to begin deployment of the UUV
The Pi 4 will sequentially send messages to the UGPSControl, WinchDown and WinchUp topics on the ROS network
Each subsystem listens to one of the three topics and deploys accordingly
After each deployment, a “finished” message is sent to the Status topic which the Pi 4 is listening to in order to know which subsystem to deploy next
UNDERWATER “GPS” SYSTEM
Special Thanks to NUWC Division Keyport: Thai Tran and Dr. Martin Renken
UNH: Laura Gustafson, Kelly Danforth, Scott Campbell, and the Olson Center
SKID - Design
Purpose: Attached skid for sensor and controller housing
Support the 22 lb. UUV in air
House three 4-inch BlueRobotics payload tubes,
control hardware and sensor housing
House two 8-inch payload tubes
  future sensor housing
Rings were designed to hold the payload tubes in the skid
Initial inspiration from BlueRobotics skid
Adapted design has increased height to meet constraints